ONTARIO REGULATION 307/00

made under the

HigHway Traffic Act

Made: May 17, 2000
Filed: May 19, 2000

Amending Reg. 612 of R.R.O. 1990

(School Buses)

1. (1) Clause 1 (1) (d) of Regulation 612 of the Revised Regulations of Ontario, 1990 is revoked and the following substituted:

(d)	be equipped with a first aid kit,

(i)	in the case of a school bus manufactured in accordance with Canadian Standards Association Standard D250–98, that complies with that Standard, or

(ii)	in the case of a school bus not manufactured in accordance with Canadian Standards Association Standard D250–98, that, unless it complies with that Standard, consists of a sturdy dustproof metal or plastic container containing,

(A)	four packets each containing four hand cleansers and 12 gauze cleansing pads,

(B)	150 individually wrapped 25 millimetre by 75 millimetre adhesive dressings,

(C)	eight 50 millimetre compress dressings,

(D)	six 100 millimetre compress dressings,

(E)	two eye dressing kits each containing one eye shield and two gauze pads,

(F)	three four–ply gauze dressings at least 900 millimetres square,

(G)	two 50 millimetre by 5.5 metre gauze bandages,

(H)	one packet of 25 millimetre by 4.6 metre adhesive tape,

(I)	six triangular bandages,

(J)	one 70 millimetre by 610 millimetre rolled metal splint,

(K)	one pair of scissors,

(L)	one pair of sliver tweezers, and

(M)	twelve 50 millimetre safety pins;

(2) Clause 1 (1) (e) of the Regulation is revoked and the following substituted:

(e)	be equipped with an interior mirror designed and adjusted to provide the seated driver with a view of the passengers, and,

(i)	in the case of a school bus manufactured on or after November 30, 1997, comply with Canada Motor Vehicle Safety Standard 111 as it read when the school bus was manufactured, including being equipped with,

(A)	two rear–view exterior mirrors on each side of the bus, one flat and one convex, and

(B)	two convex cross–view exterior mirrors consisting of one mirror on each front corner of the school bus, or

(ii)	in the case of a school bus manufactured before November 30, 1997, having a seating capacity for 24 or more passengers, be equipped with,

(A)	a convex cross–over exterior mirror, at least 190 millimetres in diameter, securely mounted and adjusted so that the seated driver may see the reflection of the area immediately in front of the front bumper of the bus,

(B)	a convex right front side–view exterior mirror, securely mounted and adjusted on the roof, right windshield corner post or exterior right rear–view mirror so that the seated driver may observe the reflection of the ground surface immediately adjacent to the right front wheel of the bus, and

(C)	exterior mirrors securely mounted and adjusted on each side of the vehicle in such a position to afford the seated driver a clearly reflected view of the roadway in the rear and of any vehicle approaching from the rear;

2. Section 2 of the Regulation is revoked and the following substituted:

2. (1) No person shall operate or permit the operation of a school bus registered in Ontario unless the school bus was manufactured in accordance with,

(a)	in the case of a school bus manufactured on or after December 1, 1982 and before September 1, 1987, Canadian Standards Association Standard D250–M 1982 or D250–M 1985;

(b)	in the case of a school bus manufactured on or after September 1, 1987 and before June 1, 2000, Canadian Standards Association Standard D250–M 1985 or D250–98;

(c)	in case of a school bus manufactured on or after June 1, 2000, Canadian Standards Association Standard D250–98.

(2) No person shall operate or permit the operation of a school bus registered in Ontario and manufactured in accordance with Canadian Standards Association Standard D250–98 unless the school bus continues to meet that Standard.

3.  Clause 3 (1) (a) of the Regulation is revoked.

4. The Regulation is amended by adding the following section:

6. For the purposes of this Regulation, the date that a school bus was manufactured shall be deemed, in the absence of evidence to the contrary, to be the date on the school bus’s compliance label.

5. This Regulation comes into force on June 1, 2000.

Back to top