ontario regulation 435/08

made under the

highway traffic act

Made: December 3, 2008
Filed: December 9, 2008
Published on e-Laws: December 10, 2008
Printed in The Ontario Gazette: December 27, 2008

Amending O. Reg. 413/05

(Vehicle Weights and Dimensions — For Safe, Productive and Infrastructure-Friendly Vehicles)

1.  Ontario Regulation 413/05 is amended by adding the following section immediately before the heading “Preconditions for Vehicle Combinations to be Designated Combinations”:

Dimensional deviations from designated combinations 1, 2 and 3

4.1  (1)  Until January 1, 2020, a vehicle combination shall be deemed to be designated combination 1 if the semi-trailer,

(a)	was built before 2006;

(b)	is not more than 14.65 metres long; and

(c)	meets every requirement of subsection 3 (1) to be a semi-trailer in designated combination 1 except for the dimensional limits for wheelbase, effective rear overhang, inter-vehicle-unit distance and track width.

(2)  A vehicle combination shall be deemed to be designated combination 2 if the semi-trailer,

(a)	was built before 2006;

(b)	is not more than 14.65 metres long; and

(c)	meets every requirement of subsection 3 (1) to be a semi-trailer in designated combination 2 except for the dimensional limits for wheelbase and track width.

(3)  A vehicle combination shall be deemed to be designated combination 3 if the semi-trailer,

(a)	was built before 2006;

(b)	is not more than 14.65 metres long; and

(c)	meets every requirement of subsection 3 (1) to be a semi-trailer in designated combination 3 except for the dimensional limits for wheelbase and track width.

2.  The Regulation is amended by adding the following sections:

Maximum allowable gross vehicle weights — single unit vehicles

36.1  (1)  The following maximum allowable gross vehicle weights are prescribed for single unit vehicles for the purposes of section 118 of the Act:

1.	For a two axle vehicle, 14,000 kilograms.

2.	For a three axle vehicle, the weight in Column 2 of the following Table corresponding to the rear axle spacing in Column 1 of the Table.

3.	For a four axle vehicle, 25,000 kilograms.

TABLE
Maximum allowable gross vehicle weight for three axle single unit vehicle for the purpose of paragraph 2 of this subsection

| Column 1 | Column 2 |
| --- | --- |
| Rear Axle Spacing (Metres) | Maximum Allowable Gross Vehicle Weight (Kilograms) |
| 1.0 to less than 1.2 | 20,000 |
| 1.2 to less than 1.3 | 21,500 |
| 1.3 to less than 1.4 | 22,000 |
| 1.4 to less than 1.5 | 22,300 |
| 1.5 to less than 1.6 | 22,500 |
| 1.6 to less than 1.7 | 23,000 |
| 1.7 to less than 1.8 | 23,500 |
| 1.8 or more | 24,000 |

(2)  A single unit vehicle whose maximum gross vehicle weight is within the maximum prescribed under subsection (1) is exempt from sections 116, 117 and 118 of the Act.

(3)  In this section,

“single unit vehicle” means a commercial motor vehicle used for,

(a)	the transportation and dumping or spreading of sand, gravel, earth, crushed or uncut rock, slag, rubble, salt, calcium chloride, snow, ice or any mixture thereof, asphalt mixes or scrap metal, or

(b)	the transportation of raw forest products.

Exemption from all maximum weights — fire apparatus

36.2  A fire apparatus is exempt from sections 116, 117 and 118 of the Act if the fire apparatus does not exceed the axle unit, axle group or gross vehicle weight ratings specified by the manufacturer.

3.  Schedules 1, 2 and 3 to the Regulation are revoked and the following substituted:

Schedule 1
Designated Combination 1 — Tractor Fixed Axle Semi-Trailer

Configuration Description

Designated Combination 1 is composed of a tractor and a single semi-trailer. The front axle of the tractor is a single axle with single tires. The drive axle of the tractor is either a single or tandem axle. The semi-trailer has one axle unit that is either a single, tandem or tridem axle.

Qualifying Preconditions

Weight, see s. 14

Equipment and components, see ss. 5 to 8

Dimensional Deviations

See s. 4.1

Dimensional Limit Chart

|  | Ref | Feature | Dimensional Limit |
| --- | --- | --- | --- |
| Overall | (1) | Overall Length | Max. 23.0m |
|  | (2) | Width | Max. 2.6m |
|  | (3) | Height | Max. 4.15m |
| Tractor | (4) | Inter-axle Spacing | Min. 3.0m |
|  | (5) | Tandem Axle Spread | 1.2 to 1.85m |
|  | (6) | Wheelbase | Max. 6.2m if tractor built in or after 2006 |
|  | (6) | Wheelbase — (long combination) | Max. 6.2m |
| Semi-Trailer | (8) | Length | Max. 14.65m |
|  | (8) | Length (long combination) | Max. 16.2m |
|  | (9) | End-Dump Semi-Trailer Bed Length | Max. 14.65m |
|  | (10) | Swing Radius | Max. 2.0m |
|  | (11) | Wheelbase | 6.25 to 12.5m |
|  | (12) | Effective Rear Overhang | Max. 35% of wheelbase |
|  | (13) | Inter-vehicle-unit Distance |  |
|  |  | – single to single, tandem or tridem | Min. 3.0m |
|  |  | – tandem to tandem | Min. 5.0m |
|  |  | – tandem to tridem | Min. 5.5m |
|  | (16) | Tandem Spread | 1.2 to 3.1m |
|  | (16) | Tridem Spread | 2.4 to 3.7m |
|  | (19) | Track Width |  |
|  |  | – trailer with single tires built before 2010 | 2.3 to 2.6m |
|  |  | – all other trailers | 2.5 to 2.6m |

Weight Limit Chart

|  | Feature | Weight Limit |
| --- | --- | --- |
| Axle Weights | Front Axle | Max. 7,700 kg (see s. 18) |
|  | Single Axle (dual tires) | Max. 10,000 kg |
|  | Tandem Axle (by axle spread) |  |
|  | 1.2 < 1.6m | Max. 18,000 kg |
|  | 1.6 < 1.7m | Max. 18,300 kg |
|  | 1.7 < 1.8m | Max. 18,700 kg |
|  | 1.8m to 3.1m | Max. 19,100 kg |
|  | Tridem Axle (by axle spread) |  |
|  | 2.4 < 2.8m | Max. 21,300 kg |
|  | 2.8 < 2.9m | Max. 21,700 kg |
|  | 2.9 < 3.0m | Max. 22,000 kg |
|  | 3.0 < 3.6m | Max. 24,000 kg |
|  | 3.6 to 3.7m | Max. 26,000 kg |
|  | Non-steering individual axle with single tires by tire width (long combinations and combinations where semi-trailer is built after 2005) |  |
|  | Less than 350 mm | Max. 6000 kg |
|  | 350 < 375 mm | Max. 7000 kg |
|  | 375 < 400 mm | Max. 7500 kg |
|  | 400 < 425 mm | Max. 8000 kg |
|  | 425 < 445 mm | Max. 8500 kg |
|  | 445 < 450 mm | Max. 8900 kg |
|  | 450 mm or more | Max. 9000 kg |
| Maximum Allowable Gross Vehicle Weight |  | see ss. 20 and 24 |

Schedule 2
Designated Combination 2 — Tractor Self-Steer Triaxle Semi-Trailer

Configuration Description

Designated Combination 2 is composed of a tractor and a single semi-trailer. The front axle of the tractor is a single axle with single tires. The drive axle of the tractor is a tandem axle. The semi-trailer has two axle units: a single self-steer axle (in front) and a tandem axle (in the rear).

Qualifying Preconditions

Weight, see s. 14

Equipment and components, see ss. 5 to 10

Labelling, see s. 13

Alternatives

Designated combination 1 (see s. 4)

Dimensional Deviations

see s. 4.1

Dimensional Limit Chart

|  | Ref | Feature | Dimensional Limit |
| --- | --- | --- | --- |
| Overall | (1) | Overall Length | Max. 23.0m |
|  | (2) | Width | Max. 2.6m |
|  | (3) | Height | Max. 4.15m |
| Tractor | (4) | Inter-axle Spacing | Min. 3.0 m |
|  | (5) | Tandem Axle Spread | 1.2 to 1.85m |
|  | (6) | Wheelbase | Max. 6.2m if tractor built in or after 2006 |
|  | (6) | Wheelbase — (long combination) | Max. 6.2m |
| Semi-Trailer | (8) | Length | Max. 14.65m |
|  | (8) | Length (long combination) | Max. 16.2m |
|  | (9) | End-Dump Semi-Trailer Bed Length | Max. 14.65m |
|  | (10) | Swing Radius | Max. 2.0m |
|  | (11) | Wheelbase | 6.25 to 12.5m |
|  | (12) | Effective Rear Overhang | Max. 35% of wheelbase |
|  | (13) | Inter-vehicle-unit Distance | Min. 4.0m if trailer built in or after 2006 |
|  | (15) | Inter-axle Spacing | > 2.5 to 3.0m |
|  | (16) | Tandem Spread | 1.2 to 2.8m |
|  | (19) | Track Width — tandem |  |
|  |  | – trailer with single tires built before 2010 | 2.3 to 2.6m |
|  |  | – all other trailers | 2.5 to 2.6m |

Weight Limit Chart

|  | Feature | Weight Limit |
| --- | --- | --- |
| Axle Weights | Front Axle | Max. 7,700 kg (see s. 18) |
|  | Tandem Axle (by axle spread) |  |
|  | 1.2 < 1.6m | Max. 18,000 kg |
|  | 1.6 < 1.7m | Max. 18,300 kg |
|  | 1.7 < 1.8m | Max. 18,700 kg |
|  | 1.8m to 2.8m | Max. 19,100 kg |
|  | Non-steering individual axle with single tires by tire width (long combinations and combinations where semi-trailer is built after 2005) |  |
|  | Less than 350 mm | Max. 6000 kg |
|  | 350 < 375 mm | Max. 7000 kg |
|  | 375 < 400 mm | Max. 7500 kg |
|  | 400 < 425 mm | Max. 8000 kg |
|  | 425 <445 mm | Max. 8500 kg |
|  | 445 < 450 mm | Max. 8900 kg |
|  | 450 mm or more | Max. 9000 kg |
| Maximum Allowable Gross Vehicle Weight |  | see ss. 20 and 24 |

Schedule 3
Designated Combination 3 — Tractor Self-Steer Quad Semi-Trailer

Configuration Description

Designated Combination 3 is composed of a tractor and a single semi-trailer. The front axle of the tractor is a single axle with single tires. The drive axle of the tractor is a tandem axle. The semi-trailer has two axle units: a single self-steer axle (in front) and a tridem axle (in the rear).

Qualifying Preconditions

Weight, see s. 14

Equipment and components, see ss. 5 to 9

Labelling, see s. 13

Alternatives

Designated combination 1 (see s. 4)

Dimensional Deviations

see s. 4.1

Dimensional Limit Chart

|  | Ref | Feature | Dimensional Limit |
| --- | --- | --- | --- |
| Overall | (1) | Overall Length | Max. 23.0m |
|  | (2) | Width | Max. 2.6m |
|  | (3) | Height | Max. 4.15m |
| Tractor | (4) | Inter-axle Spacing | Min. 3.0 m |
|  | (5) | Tandem Axle Spread | 1.2 to 1.85m |
|  | (6) | Wheelbase | Max. 6.2m if tractor built in or after 2006 |
|  | (6) | Wheelbase — (long combination) | Max. 6.2m |
| Semi-Trailer | (8) | Length | Max. 14.65m |
|  | (8) | Length (long combination) | Max. 16.2m |
|  | (9) | End-Dump Semi-Trailer Bed Length | Max. 14.65m |
|  | (10) | Swing Radius | Max. 2.0m |
|  | (11) | Wheelbase | 6.25 to 12.5m |
|  | (12) | Effective Rear Overhang | Max. 35% of wheelbase |
|  | (13) | Inter-vehicle-unit Distance |  |
|  |  | – if tridem spread is 3.0 < 3.6m | Min. 6.0m |
|  |  | – if tridem spread is 3.6 to 3.7m | Min. 5.5m |
|  | (15) | Inter-axle Spacing | > 2.5 to 3.0m |
|  | (16) | Tridem Spread | 3.0 to 3.7m |
|  | (19) | Track Width — tridem |  |
|  |  | – trailer with single tires built before 2010 | 2.3 to 2.6m |
|  |  | – all other trailers | 2.5 to 2.6m |

Weight Limit Chart

|  | Feature | Weight Limit |
| --- | --- | --- |
| Tire Weights | Self-steering axle (tire width) |  |
|  | 365 < 385 mm | Max. 4,000 kg per tire |
|  | 385 mm or more | Max. 4,250 kg per tire |
| Axle Weights | Front Axle | Max. 7,700 kg (see s. 18) |
|  | Tandem Axle (by axle spread) |  |
|  | 1.2 < 1.6m | Max. 18,000 kg |
|  | 1.6 < 1.7m | Max. 18,300 kg |
|  | 1.7 < 1.8m | Max. 18,700 kg |
|  | 1.8m to 1.85m | Max. 19,100 kg |
|  | Tridem Axle (by axle spread) |  |
|  | 3.0 < 3.6m | 24,000 kg |
|  | 3.6 to 3.7m | 25,500 kg |
|  | Non-steering individual axle with single tires by tire width (long combinations and combinations where semi-trailer is built after 2005) |  |
|  | Less than 350 mm | Max. 6000 kg |
|  | 350 < 375 mm | Max. 7000 kg |
|  | 375 < 400 mm | Max. 7500 kg |
|  | 400 < 425 mm | Max. 8000 kg |
|  | 425 < 445 mm | Max. 8500 kg |
|  | 445 < 450 mm | Max. 8900 kg |
|  | 450 mm or more | Max. 9000 kg |
| Maximum Allowable Gross Vehicle Weight |  | see ss. 20 and 24 |

4.  (1)  The Dimensional Limit Chart in Schedule 4 to the Regulation is amended by striking out the last row and substituting the following:

|  | (19) | Track Width — tridem axle |  |
| --- | --- | --- | --- |
|  |  | – trailer with single tires built before 2010 | 2.3 to 2.6m |
|  |  | – all other trailers | 2.5 to 2.6m |

(2)  The Weight Limit Chart in Schedule 4 to the Regulation is revoked and the following substituted:

Weight Limit Chart

|  | Feature | Weight Limit |
| --- | --- | --- |
| Axle Weights | Front Axle | Max. 7,700 kg (see s. 18) |
|  | Tandem Axle (by axle spread) |  |
|  | 1.3 < 1.6m | Max. 18,000 kg |
|  | 1.6 < 1.7m | Max. 18,300 kg |
|  | 1.7 < 1.8m | Max. 18,700 kg |
|  | 1.8m to 1.85m | Max. 19,100 kg |
|  | Tridem Axle | Max. 22,500 kg |
|  | Non-steering individual axle with single tires by tire width (long combinations and combinations where semi-trailer is built after 2005) |  |
|  | Less than 350 mm | Max. 6000 kg |
|  | 350 < 375 mm | Max. 7000 kg |
|  | 375 < 400 mm | Max. 7500 kg |
|  | 400 < 425 mm | Max. 8000 kg |
|  | 425 < 445 mm | Max. 8500 kg |
|  | 445 < 450 mm | Max. 8900 kg |
|  | 450 mm or more | Max. 9000 kg |
| Maximum Allowable Gross Vehicle Weight |  | see ss. 20 and 24 |

5.  (1)  The Dimensional Limit Chart in Schedule 5 to the Regulation is amended by striking out the last row and substituting the following:

|  | (19) | Track Width — tridem axle |  |
| --- | --- | --- | --- |
|  |  | – trailer with single tires built before 2010 | 2.3 to 2.6m |
|  |  | – all other trailers | 2.5 to 2.6m |

(2)  The Weight Limit Chart in Schedule 5 to the Regulation is revoked and the following substituted:

Weight Limit Chart

|  | Feature | Weight Limit |
| --- | --- | --- |
| Axle Weights | Front Axle | Max. 7,700 kg (see s. 18) |
|  | Tandem Axle (by axle spread) |  |
|  | 1.3 < 1.6m | Max. 18,000 kg |
|  | 1.6 < 1.7m | Max. 18,300 kg |
|  | 1.7 < 1.8m | Max. 18,700 kg |
|  | 1.8m to 1.85m | Max. 19,100 kg |
|  | Tridem Axle | Max. 22,500 kg |
|  | Non-steering individual axle with single tires by tire width (long combinations and combinations where semi-trailer is built after 2005) |  |
|  | Less than 350 mm | Max. 6000 kg |
|  | 350 < 375 mm | Max. 7000 kg |
|  | 375 < 400 mm | Max. 7500 kg |
|  | 400 < 425 mm | Max. 8000 kg |
|  | 425 < 445 mm | Max. 8500 kg |
|  | 445 < 450 mm | Max. 8900 kg |
|  | 450 mm or more | Max. 9000 kg |
| Maximum Allowable Gross Vehicle Weight |  | see ss. 20 and 24 |

6.  (1)  The Dimensional Limit Chart in Schedule 6 to the Regulation is amended by striking out the last two rows and substituting the following:

|  | (17) | Inter-axle Spacing | 2.3 to 2.8m |
| --- | --- | --- | --- |
|  | (19) | Track Width — quadruple axle |  |
|  |  | – trailer with single tires built before 2010 | 2.3 to 2.6m |
|  |  | – all other trailers | 2.5 to 2.6m |

(2)  The Weight Limit Chart in Schedule 6 to the Regulation is revoked and the following substituted:

Weight Limit Chart

|  | Feature | Weight Limit |
| --- | --- | --- |
| Axle Weights | Front Axle | Max. 7,700 kg (see s. 18) |
|  | Tandem Axle (by axle spread) |  |
|  | 1.3 < 1.6m | Max. 18,000 kg |
|  | 1.6 < 1.7m | Max. 18,300 kg |
|  | 1.7 < 1.8m | Max. 18,700 kg |
|  | 1.8m to 1.85m | Max. 19,100 kg |
|  | Quadruple Axle | Max. 26,000 kg |
|  | Non-steering individual axle with single tires by tire width (long combinations and combinations where semi-trailer is built after 2005) |  |
|  | Less than 350 mm | Max. 6000 kg |
|  | 350 < 375 mm | Max. 7000 kg |
|  | 375 < 400 mm | Max. 7500 kg |
|  | 400 < 425 mm | Max. 8000 kg |
|  | 425 < 445 mm | Max. 8500 kg |
|  | 445 < 450 mm | Max. 8900 kg |
|  | 450 mm or more | Max. 9000 kg |
| Maximum Allowable Gross Vehicle Weight |  | see ss. 20 and 24 |

7.  (1)  The Dimensional Limit Chart in Schedule 7 to the Regulation is amended by striking out the last row and substituting the following:

|  | (19) | Track Width — quadruple axle |  |
| --- | --- | --- | --- |
|  |  | – trailer with single tires built before 2010 | 2.3 to 2.6m |
|  |  | – all other trailers | 2.5 to 2.6m |

(2)  The Weight Limit Chart in Schedule 7 to the Regulation is revoked and the following substituted:

Weight Limit Chart

|  | Feature | Weight Limit |
| --- | --- | --- |
| Axle Weights | Front Axle | Max. 7,700 kg (see s. 18) |
|  | Tandem Axle (by axle spread) |  |
|  | 1.3 < 1.6m | Max. 18,000 kg |
|  | 1.6 < 1.7m | Max. 18,300 kg |
|  | 1.7 < 1.8m | Max. 18,700 kg |
|  | 1.8m to 1.85m | Max. 19,100 kg |
|  | Quadruple Axle | Max. 26,000 kg |
|  | Non-steering individual axle with single tires by tire width (long combinations and combinations where semi-trailer is built after 2005) |  |
|  | Less than 350 mm | Max. 6000 kg |
|  | 350 < 375 mm | Max. 7000 kg |
|  | 375 < 400 mm | Max. 7500 kg |
|  | 400 < 425 mm | Max. 8000 kg |
|  | 425 < 445 mm | Max. 8500 kg |
|  | 445 < 450 mm | Max. 8900 kg |
|  | 450 mm or more | Max. 9000 kg |
| Maximum Allowable Gross Vehicle Weight |  | see ss. 20 and 24 |

8.  (1)  The Dimensional Limit Chart in Schedule 8 to the Regulation is revoked and the following substituted:

Dimensional Limit Chart

|  | Ref | Feature | Dimensional Limit |
| --- | --- | --- | --- |
| Overall | (1) | Overall Length | Max. 23.0m |
|  | (1) | Overall Length (long combination) | Max. 23.5m |
|  | (2) | Width | Max. 2.6m |
|  | (3) | Height | Max. 4.15m |
| Tractor | (4) | Inter-axle Spacing | not controlled |
|  | (5) | Tridem Axle Spread | 2.4 to 2.8m |
|  | (6) | Wheelbase | 6.6 to 6.8m |
|  | (7) | Tridem Track Width |  |
|  |  | – tractor with single tires built before 2010 | 2.3 to 2.6m |
|  |  | – all other tractors | 2.5 to 2.6m |
| Semi-Trailer | (8) | Length | Max. 14.65m |
|  | (8) | Length (long combination) | Max. 16.2m |
|  | (9) | End-Dump Semi-Trailer Bed Length | Max. 14.65m |
|  | (10) | Swing Radius | Max. 2.0m |
|  | (11) | Wheelbase | 6.25 to 12.0m |
|  | (12) | Effective Rear Overhang | Max. 35% of wheelbase |
|  | (13) | Inter-vehicle-unit Distance |  |
|  |  | – single to tridem | Min. 3.0m |
|  |  | – tandem to tridem | Min. 5.5m |
|  |  | – tridem to tridem | Min. 6.0m |
|  | (16) | Tandem Spread | 1.2 to 3.1m |
|  | (16) | Tridem Spread | 2.4 to 3.7m |
|  | (19) | Track Width |  |
|  |  | – trailer with single tires built before 2010 | 2.3 to 2.6m |
|  |  | – all other trailers | 2.5 to 2.6m |

(2)  The Weight Limit Chart in Schedule 8 to the Regulation is revoked and the following substituted:

Weight Limit Chart

|  | Feature | Weight Limit |
| --- | --- | --- |
| Axle Weights | Front Axle | Max. 7,700 kg (see s. 18) |
|  | Tri-drive Axle (by axle spread) |  |
|  | 2.4 < 2.7m | Max. 21,300 kg |
|  | 2.7 to 2.8m | Max. 22,000 kg |
|  | Single Axle (dual tires) | Max. 10,000 kg |
|  | Tandem Axle (by axle spread) |  |
|  | 1.2 < 1.6m | Max. 18,000 kg |
|  | 1.6 < 1.7m | Max. 18,300 kg |
|  | 1.7 < 1.8m | Max. 18,700 kg |
|  | 1.8m to 3.1m | Max. 19,100 kg |
|  | Tridem Axle (by axle spread) |  |
|  | 2.4 < 2.8m | Max. 21,300 kg |
|  | 2.8 < 2.9m | Max. 21,700 kg |
|  | 2.9 < 3.0m | Max. 22,000 kg |
|  | 3.0 < 3.6m | Max. 24,000 kg |
|  | 3.6 to 3.7m | Max. 26,000 kg |
|  | Non-steering individual axle with single tires by tire width (long combinations and combinations where semi-trailer is built after 2005) |  |
|  | Less than 350 mm | Max. 6000 kg |
|  | 350 < 375 mm | Max. 7000 kg |
|  | 375 < 400 mm | Max. 7500 kg |
|  | 400 < 425 mm | Max. 8000 kg |
|  | 425 < 445 mm | Max. 8500 kg |
|  | 445 < 450 mm | Max. 8900 kg |
|  | 450 mm or more | Max. 9000 kg |
| Maximum Allowable Gross Vehicle Weight |  | see ss. 20 and 24 |

9.  (1)  The Dimensional Limit Chart in Schedule 9 to the Regulation is revoked and the following substituted:

Dimensional Limit Chart

|  | Ref | Feature | Dimensional Limit |
| --- | --- | --- | --- |
| Overall | (1) | Overall Length | Max. 23.0m |
|  | (1) | Overall Length (long combination) | Max. 23.5m |
|  | (2) | Width | Max. 2.6m |
|  | (3) | Height | Max. 4.15m |
| Tractor | (4) | Inter-axle Spacing | not controlled |
|  | (5) | Tridem Axle Spread | 2.4 to 2.8m |
|  | (6) | Wheelbase | 6.6 to 6.8m |
|  | (7) | Tridem Track Width |  |
|  |  | – tractor with single tires built before 2010 | 2.3 to 2.6m |
|  |  | – all other tractors | 2.5 to 2.6m |
|  | (8) | Length (long combination) | Max. 16.2m |
|  | (9) | End-Dump Semi-Trailer Bed Length | Max. 14.65m |
|  | (10) | Swing Radius | Max. 2.0m |
|  | (11) | Wheelbase | 6.25 to 12.0m |
|  | (12) | Effective Rear Overhang | Max. 35% of wheelbase |
|  | (13) | Inter-vehicle-unit Distance | Min. 3.7m |
|  | (15) | Inter-axle Spacing | >2.5 to 3.0m |
|  | (16) | Tandem Spread | 1.2 to 2.8m |
|  | (19) | Track Width — tandem |  |
|  |  | – trailer with single tires built before 2010 | 2.3 to 2.6m |
|  |  | – all other trailers | 2.5 to 2.6m |

(2)  The Weight Limit Chart in Schedule 9 to the Regulation is revoked and the following substituted:

Weight Limit Chart

|  | Feature | Weight Limit |
| --- | --- | --- |
| Axle Weights | Front Axle | Max. 7,700 kg (see s. 18) |
|  | Tri-drive Axle (by axle spread) |  |
|  | 2.4 < 2.7m | Max. 21,300 kg |
|  | 2.7 to 2.8m | Max. 22,000 kg |
|  | Tandem Axle (by axle spread) |  |
|  | 1.2 < 1.6m | Max. 18,000 kg |
|  | 1.6 < 1.7m | Max. 18,300 kg |
|  | 1.7 < 1.8m | Max. 18,700 kg |
|  | 1.8m to 2.8m | Max. 19,100 kg |
|  | Non-steering individual axle with single tires by tire width (long combinations and combinations where semi-trailer is built after 2005) |  |
|  | Less than 350 mm | Max. 6000 kg |
|  | 350 < 375 mm | Max. 7000 kg |
|  | 375 < 400 mm | Max. 7500 kg |
|  | 400 < 425 mm | Max. 8000 kg |
|  | 425 < 445 mm | Max. 8500 kg |
|  | 445 < 450 mm | Max. 8900 kg |
|  | 450 mm or more | Max. 9000 kg |
| Maximum Allowable Gross Vehicle Weight |  | see ss. 20 and 24 |

10.  (1)  The Dimensional Limit Chart in Schedule 10 to the Regulation is revoked and the following substituted:

Dimensional Limit Chart

|  | Ref | Feature | Dimensional Limit |
| --- | --- | --- | --- |
| Overall | (1) | Overall Length | Max. 23.0m |
|  | (1) | Overall Length (long combination) | Max. 23.5m |
|  | (2) | Width | Max. 2.6m |
|  | (3) | Height | Max. 4.15m |
| Tractor | (4) | Inter-axle Spacing | not controlled |
|  | (5) | Tridem Axle Spread | 2.4 to 2.8m |
|  | (6) | Wheelbase | 6.6 to 6.8m |
|  | (7) | Tridem Track Width |  |
|  |  | – tractor with single tires built before 2010 | 2.3 to 2.6m |
|  |  | – all other tractors | 2.5 to 2.6m |
| Semi-Trailer | (8) | Length | Max. 14.65m |
|  | (8) | Length (long combination) | Max. 16.2m |
|  | (9) | End-Dump Semi-Trailer Bed Length | Max. 14.65m |
|  | (10) | Swing Radius | Max. 2.0m |
|  | (11) | Wheelbase | 6.25 to 12.0m |
|  | (12) | Effective Rear Overhang | Max. 35% of wheelbase |
|  | (13) | Inter-vehicle-unit Distance |  |
|  |  | – if tridem spread is 3.0 < 3.6m | Min. 5.0m |
|  |  | – if tridem spread is 3.6 to 3.7m | Min. 4.5m |
|  | (15) | Inter-axle Spacing | >2.5 to 3.0m |
|  | (16) | Tridem Spread | 3.0 to 3.7m |
|  | (19) | Track Width — tridem |  |
|  |  | – trailer with single tires built before 2010 | 2.3 to 2.6m |
|  |  | – all other trailers | 2.5 to 2.6m |

(2)  The Weight Limit Chart in Schedule 10 to the Regulation is revoked and the following substituted:

Weight Limit Chart

|  | Feature | Weight Limit |
| --- | --- | --- |
| Tire Weights | Self-steer axle (tire width) |  |
|  | 365 < 385 mm | Max. 4,000 kg per tire |
|  | 385 mm or more | Max. 4,250 kg per tire |
| Axle Weights | Front Axle | Max. 7,700 kg (see s. 18) |
|  | Tri-drive Axle (by axle spread) |  |
|  | 2.4 < 2.7m | Max. 21,300 kg |
|  | 2.7 to 2.8m | Max. 22,000 kg |
|  | Tridem Axle (by axle spread) |  |
|  | 3.0 < 3.6m | 24,000 kg |
|  | 3.6 to 3.7m | 25,500 kg |
|  | Non-steering individual axle with single tires by tire width (long combinations and combinations where semi-trailer is built after 2005) |  |
|  | Less than 350 mm | Max. 6000 kg |
|  | 350 < 375 mm | Max. 7000 kg |
|  | 375 < 400 mm | Max. 7500 kg |
|  | 400 < 425 mm | Max. 8000 kg |
|  | 425 < 445 mm | Max. 8500 kg |
|  | 445 < 450 mm | Max. 8900 kg |
|  | 450 mm or more | Max. 9000 kg |
| Maximum Allowable Gross Vehicle Weight |  | see ss. 20 and 24 |

11.  (1)  The Dimensional Limit Chart in Schedule 11 to the Regulation is revoked and the following substituted:

Dimensional Limit Chart

|  | Ref | Feature | Dimensional Limit |
| --- | --- | --- | --- |
| Overall | (1) | Overall Length | Max. 23.0m |
|  | (1) | Overall Length (long combination) | Max. 25.0m |
|  | (2) | Width | Max. 2.6m |
|  | (3) | Height | Max. 4.15m |
| Tractor | (4) | Inter-axle Spacing | Min. 3.0m |
|  | (5) | Tandem Axle Spread | 1.2 to 1.85m |
|  | (6) | Wheelbase | Max. 6.2m if tractor built in or after 2006 |
|  | (6) | Wheelbase — (long combination) | Max. 6.2m |
| Lead Semi- | (10) | Swing Radius | Max. 2.0m |
| Trailer | (11) | Wheelbase | Min. 6.25m |
|  | (13) | Inter-vehicle-unit Distance |  |
|  |  | – single to single or tandem | Min. 3.0m |
|  |  | – tandem to tandem | Min. 5.0m |
|  | (16) | Tandem Spread | 1.2 to 1.85m |
|  | (18) | Hitch Offset | Max. 1.8m |
|  | (19) | Track Width |  |
|  |  | – trailer with single tires built before 2010 | 2.3 to 2.6m |
|  |  | – all other trailers | 2.5 to 2.6m |
| Trailer | (20) | Box Length | Max. 18.5m |
| Combination | (20) | Box Length (long combination) | Max. 20.0m |
|  | (21) | Converter Dolly Drawbar Length | not controlled |
|  | (22) | Converter Dolly Track Width |  |
|  |  | – converter dolly with single tires built before 2010 | 2.3 to 2.6m |
|  |  | – all other converter dollies | 2.5 to 2.6m |
| Second Semi or | (25) | Wheelbase | Min. 6.25m |
| Full Trailer | (26) | Inter-vehicle-unit Distance | not controlled |
|  | (27) | Inter-axle Spacing | Min. 3.0m |
|  | (28) | Tandem Spread | 1.2 to 1.85m |
|  | (29) | Track Width |  |
|  |  | – trailer with single tires built before 2010 | 2.3 to 2.6m |
|  |  | – all other trailers | 2.5 to 2.6m |

(2)  The Weight Limit Chart in Schedule 11 to the Regulation is revoked and the following substituted:

Weight Limit Chart

|  | Feature | Weight Limit |
| --- | --- | --- |
| Axle Weights | Front Axle | Max. 7,700 kg (see s. 18) |
|  | Single Axle (dual tires) | Max. 10,000 kg |
|  | Tandem Axle (by axle spread) |  |
|  | 1.2 < 1.6m | Max. 18,000 kg |
|  | 1.6 < 1.7m | Max. 18,300 kg |
|  | 1.7 < 1.8m | Max. 18,700 kg |
|  | 1.8m to 1.85m | Max. 19,100 kg |
|  | Non-steering individual axle with single tires by tire width (long combinations and combinations where any trailer is built after 2005) |  |
|  | Less than 350 mm | Max. 6000 kg |
|  | 350 < 375 mm | Max. 7000 kg |
|  | 375 < 400 mm | Max. 7500 kg |
|  | 400 < 425 mm | Max. 8000 kg |
|  | 425 < 445 mm | Max. 8500 kg |
|  | 445 < 450 mm | Max. 8900 kg |
|  | 450 mm or more | Max. 9000 kg |
| Maximum Allowable Gross Vehicle Weight |  | see ss. 21 and 24 |

12.  (1)  The Dimensional Limit Chart in Schedule 12 to the Regulation is revoked and the following substituted:

Dimensional Limit Chart

|  | Ref | Feature | Dimensional Limit |
| --- | --- | --- | --- |
| Overall | (1) | Overall Length | Max. 23.0m |
|  | (1) | Overall Length (long combination) | Max. 25.0m |
|  | (2) | Width | Max. 2.6m |
|  | (3) | Height | Max. 4.15m |
| Tractor | (4) | Inter-axle Spacing | Min. 3.0m |
|  | (5) | Tandem Axle Spread | 1.2 to 1.85m |
|  | (6) | Wheelbase | Max. 6.2m if tractor built in or after 2006 |
|  | (6) | Wheelbase — (long combination) | Max. 6.2m |
| Lead Semi- | (10) | Swing Radius | Max. 2.0m |
| Trailer | (11) | Wheelbase | Min. 6.25m |
|  | (13) | Inter-vehicle-unit Distance |  |
|  |  | – single to tandem or tridem | Min. 3.0m |
|  |  | – tandem to tandem | Min. 5.0m |
|  |  | – tandem to tridem | Min. 5.5m |
|  | (16) | Tandem Spread | 1.2 to 1.85m |
|  | (16) | Tridem Spread | 2.4 to 3.1m |
|  | (19) | Track Width |  |
|  |  | – trailer with single tires built before 2010 | 2.3 to 2.6m |
|  |  | – all other trailers | 2.5 to 2.6m |
| Trailer | (20) | Box Length | Max. 18.5m |
| Combination | (20) | Box Length (long combination) | Max. 20.0m |
|  | (11)+(25) | Sum of Trailer Wheelbases | Max. 17.0m |
| Second Trailer | (23) | Swing Radius | Max. 2.0m |
|  | (24) | Kingpin behind rearmost axle of lead trailer | Max. 0.3m |
|  | (25) | Wheelbase | Min. 6.25m |
|  | (26) | Inter-vehicle-unit Distance |  |
|  |  | – single to tandem or tridem | Min. 3.0m |
|  |  | – tandem to tandem | Min. 5.0m |
|  |  | – tandem to tridem | Min. 5.5m |
|  |  | – tridem to tridem | Min. 6.0m |
|  | (28) | Tandem Spread | 1.2 to 1.85m |
|  | (28) | Tridem Spread | 2.4 to 3.1m |
|  | (29) | Track Width |  |
|  |  | – trailer with single tires built before 2010 | 2.3 to 2.6m |
|  |  | – all other trailers | 2.5 to 2.6m |

(2)  The Weight Limit Chart in Schedule 12 to the Regulation is revoked and the following substituted:

Weight Limit Chart

|  | Feature | Weight Limit |
| --- | --- | --- |
| Axle Weights | Front Axle | Max. 7,700 kg (see s. 18) |
|  | Single Axle (dual tires) | Max. 10,000 kg |
|  | Tandem Axle (by axle spread) |  |
|  | 1.2 < 1.6m | Max. 18,000 kg |
|  | 1.6 < 1.7m | Max. 18,300 kg |
|  | 1.7 < 1.8m | Max. 18,700 kg |
|  | 1.8m to 1.85m | Max. 19,100 kg |
|  | Tridem Axle (by axle spread) |  |
|  | 2.4 < 2.8m | Max. 21,300 kg |
|  | 2.8 < 2.9m | Max. 21,700 kg |
|  | 2.9 < 3.0m | Max. 22,000 kg |
|  | 3.0 to 3.1m | Max. 24,000 kg |
|  | Non-steering individual axle with single tires by tire width (long combinations and combinations where any trailer is built after 2005) |  |
|  | Less than 350 mm | Max. 6000 kg |
|  | 350 < 375 mm | Max. 7000 kg |
|  | 375 < 400 mm | Max. 7500 kg |
|  | 400 < 425 mm | Max. 8000 kg |
|  | 425 < 445 mm | Max. 8500 kg |
|  | 445 < 450 mm | Max. 8900 kg |
|  | 450 mm or more | Max. 9000 kg |
| Maximum Allowable Gross Vehicle Weight |  | see ss. 22 and 24 |

13.  (1)  The Dimensional Limit Chart in Schedule 13 to the Regulation is revoked and the following substituted:

Dimensional Limit Chart

|  | Ref | Feature | Dimensional Limit |
| --- | --- | --- | --- |
| Overall | (1) | Overall Length | Max. 23.0m |
|  | (1) | Overall Length (long combination) | Max. 25.0m |
|  | (2) | Width | Max. 2.6m |
|  | (3) | Height | Max. 4.15m |
| Tractor | (4) | Inter-axle Spacing | Min. 3.0m |
|  | (5) | Tandem Axle Spread | 1.2 to 1.85m |
|  | (6) | Wheelbase | Max. 6.2m if tractor built in or after 2006 |
|  | (6) | Wheelbase — (long combination) | Max. 6.2m |
| Lead Semi- | (10) | Swing Radius | Max. 2.0m |
| Trailer | (11) | Wheelbase | Min. 6.25m |
|  | (13) | Inter-vehicle-unit Distance |  |
|  |  | – single to single or tandem | Min. 3.0m |
|  |  | – tandem to tandem | Min. 5.0m |
|  | (16) | Tandem Spread | 1.2 to 1.85m |
|  | (18) | Hitch Offset | Max. 1.8m |
|  | (19) | Track Width |  |
|  |  | – trailer with single tires built before 2010 | 2.3 to 2.6m |
|  |  | – all other trailers | 2.5 to 2.6m |
| Trailer | (20) | Box Length | Max. 18.5m |
| Combination | (20) | Box Length (long combination) | Max. 20.0m |
|  | (21) | Converter Dolly Drawbar Length | Max. 2.0m |
|  | (22) | Converter Dolly Track Width |  |
|  |  | – converter dolly with single tires built before 2010 | 2.3 to 2.6m |
|  |  | – all other converter dollies | 2.5 to 2.6m |
| Second Trailer | (25) | Wheelbase | Min. 6.25m |
|  | (26) | Inter-vehicle-unit Distance | not controlled |
|  | (27) | Inter axle Spacing | Min. 3.0m |
|  | (28) | Tandem Spread | 1.2 to 1.85m |
|  | (29) | Track Width |  |
|  |  | – trailer with single tires built before 2010 | 2.3 to 2.6m |
|  |  | – all other trailers | 2.5 to 2.6m |

(2)  The Weight Limit Chart in Schedule 13 to the Regulation is revoked and the following substituted:

Weight Limit Chart

|  | Feature | Weight Limit |
| --- | --- | --- |
| Axle Weights | Front Axle | Max. 7,700 kg (see s. 18) |
|  | Single Axle (dual tires) | Max. 10,000 kg |
|  | Tandem Axle (by axle spread) |  |
|  | 1.2 < 1.6m | Max. 18,000 kg |
|  | 1.6 < 1.7m | Max. 18,300 kg |
|  | 1.7 < 1.8m | Max. 18,700 kg |
|  | 1.8m to 1.85m | Max. 19,100 kg |
|  | Non-steering individual axle with single tires by tire width (long combinations and combinations where any trailer is built after 2005) |  |
|  | Less than 350 mm | Max. 6000 kg |
|  | 350 < 375 mm | Max. 7000 kg |
|  | 375 < 400 mm | Max. 7500 kg |
|  | 400 < 425 mm | Max. 8000 kg |
|  | 425 < 445 mm | Max. 8500 kg |
|  | 445 < 450 mm | Max. 8900 kg |
|  | 450 mm or more | Max. 9000 kg |
| Maximum Allowable Gross Vehicle Weight |  | see ss. 23 and 24 |

14.  Section 4.1 of the Regulation, as made by section 1, is revoked on January 1, 2020.

15.  The notes immediately before the Dimensional Limit Chart in Schedule 1, as remade by section 3, are revoked on January 1, 2020 and the following substituted:

Configuration Description

Designated Combination 1 is composed of a tractor and a single semi-trailer. The front axle of the tractor is a single axle with single tires. The drive axle of the tractor is either a single or tandem axle. The semi-trailer has one axle unit that is either a single, tandem or tridem axle.

Qualifying Preconditions

Weight, see s. 14

Equipment and components, see ss. 5 to 8

16.  The notes immediately before the Dimensional Limit Chart in Schedule 2, as remade by section 3, are revoked on January 1, 2020 and the following substituted:

Configuration Description

Designated Combination 2 is composed of a tractor and a single semi-trailer. The front axle of the tractor is a single axle with single tires. The drive axle of the tractor is a tandem axle. The semi-trailer has two axle units: a single self-steer axle (in front) and a tandem axle (in the rear).

Qualifying Preconditions

Weight, see s. 14

Equipment and components, see ss. 5 to 10

Labelling, see s. 13

Alternatives

Designated combination 1 (see s. 4)

17.  The notes immediately before the Dimensional Limit Chart in Schedule 3, as remade by section 3, are revoked on January 1, 2020 and the following substituted:

Configuration Description

Designated Combination 3 is composed of a tractor and a single semi-trailer. The front axle of the tractor is a single axle with single tires. The drive axle of the tractor is a tandem axle. The semi-trailer has two axle units: a single self-steer axle (in front) and a tridem axle (in the rear).

Qualifying Preconditions

Weight, see s. 14

Equipment and components, see ss. 5 to 9

Labelling, see s. 13

Alternatives

Designated combination 1 (see s. 4)

18.  This Regulation comes into force on the day it is filed.

Back to top