ontario regulation 306/17

made under the

Environmental Protection Act

Made: July 26, 2017
Filed: July 28, 2017
Published on e-Laws: July 31, 2017
Printed in The Ontario Gazette: August 12, 2017

Amending O. Reg. 560/94

(EFFLUENT MONITORING AND EFFLUENT LIMITS - METAL MINING SECTOR)

1.  Schedules 1 to 3 of Ontario Regulation 560/94 are revoked and the following substituted:

Schedule 1
Process Effluent Limits and Monitoring Frequency (All existing and new plants)

| Item | Column 0.1 Analytical test group | Column 1 Parameter | Column 2 Monitoring frequency | Column 3 Daily concentration limit (mg/L) | Column 4 Monthly average concentration limit |
| --- | --- | --- | --- | --- | --- |
| 1. | 2 | Total Cyanide | Thrice weekly | 2 | 1 |
| 2. | 8 | Total Suspended Solids (TSS) | Thrice weekly | 30 | 15 |
| 3. | 9 | Copper | Weekly | 0.6 | 0.3 |
| 4. | 9 | Lead | Weekly | 0.4 | 0.2 |
| 5. | 9 | Nickel | Weekly | 1 | 0.5 |
| 6. | 9 | Zinc | Weekly | 1 | 0.5 |
| 7. | 10 | Arsenic | Weekly | 1 | 0.5 |

SCHEDULE 2
Cooling Water Effluent Assessment Monitoring (All existing and new Plants)

| Item | Column 0.1 Analytical test group | Column 1 Parameter | Column 2 Monitoring frequency |
| --- | --- | --- | --- |
| 1. | 8 | Total Suspended Solids (TSS) | Weekly |

Schedule 3
Overflow Effluent Assessment Monitoring (All Existing and New Plants)

| Item | Column 0.1 Analytical test group | Column 1 Parameter | Column 2 Monitoring frequency |
| --- | --- | --- | --- |
| 1. | 2 | Total Cyanide | Every eight-hour period |
| 2. | 8 | Total Suspended Solids (TSS) | Every eight-hour period |
| 3. | 9 | Copper | Every eight-hour period |
| 4. | 9 | Lead | Every eight-hour period |
| 5. | 9 | Nickel | Every eight-hour period |
| 6. | 9 | Zinc | Every eight-hour period |
| 7. | 10. | Arsenic | Every eight-hour period |

Commencement

2.  This Regulation comes into force on the day it is filed.

Back to top