ontario regulation 310/17

made under the

Environmental Protection Act

Made: July 26, 2017
Filed: July 28, 2017
Published on e-Laws: July 31, 2017
Printed in The Ontario Gazette: August 12, 2017

Amending O. Reg. 215/95

(EFFLUENT MONITORING AND EFFLUENT LIMITS - ELECTRIC POWER GENERATION SECTOR)

1.  (1)  Clause (a) of the definition of “limited parameter” in subsection 1 (1) of Ontario Regulation 215/95 is amended by striking out “Schedule 2 for the plant” and substituting “the Table for the plant in Schedule 2”.

(2)  Clause (b) of the definition of “limited parameter” in subsection 1 (1) of the Regulation is amended by striking out “Schedule 3 for the plant” and substituting “the Table for the plant in Schedule 3”.

2.  (1)  Subsection 16 (1) of the Regulation is amended by adding “the Table for the plant in” before “Schedule 2”.

(2)  Subsection 16 (2) of the Regulation is amended by adding “the Table for the plant in” before “Schedule 2”.

(3)  Clause 16 (3) (a) of the Regulation is amended by adding “the Table for the plant in” before “Schedule 2”.

(4)  Clause 16 (3) (b) of the Regulation is amended by adding “the Table for the plant in” before “Schedule 2”.

(5)  Subsection 16 (4) of the Regulation is amended by adding “the Table for the plant in” before “Schedule 3”.

(6)  Subsection 16 (5) of the Regulation is amended by adding “the Table for the plant in” before “Schedule 3”.

3.  (1)  Subsection 19 (1) of the Regulation is amended by striking out “Schedule 2 for the discharger’s plant” and substituting “the Table for the discharger’s plant in Schedule 2”.

(2)  Subsection 19 (4) of the Regulation is amended by striking out “Schedule 2 of the discharger’s plant” and substituting “the Table for the discharger’s plant in Schedule 2”.

4.  (1)  Subsection 20 (1) of the Regulation is amended by striking out “Schedule 2 for the discharger’s plant” and substituting “the Table for the discharger’s plant in Schedule 2”.

(2)  Subsection 20 (5) of the Regulation is amended by striking out “Schedule 2 of the discharger’s plant” and substituting “the Table for the discharger’s plant in Schedule 2”.

5.  (1)  Subsection 21 (1) of the Regulation is amended by striking out “Schedule 3 for the discharger’s plant” and substituting “the Table for the discharger’s plant in Schedule 3”.

(2)  Subsection 21 (11) of the Regulation is amended by adding “the Table for the discharger’s plant in” before “Schedule 3”.

(3)  Subsection 21 (12) of the Regulation is amended by adding “the Table for the discharger’s plant in” before “Schedule 3”.

(4)  Subsection 21 (20) of the Regulation is amended by striking out “Schedule 3 for the discharger’s plant” and substituting “the Table for the discharger’s plant in Schedule 3”.

6.  (1)  Subsection 22 (1) of the Regulation is amended by striking out “Schedule 2 for the discharger’s plant” and substituting “the Table for the discharger’s plant in Schedule 2”.

(2)  Subsection 22 (2) of the Regulation is amended by striking out “Schedule 2 for the discharger’s plant” and substituting “the Table for the discharger’s plant in Schedule 2”.

7.  Schedules 2 and 3 of the Regulation are revoked and the following substituted:

Schedule 2
Types Of Non-Event Process Effluent Streams, Limits, Monitoring Frequency

Table 1
PLANT: Atikokan TGS

| Item | Analytical Test Group | Column 1 Parameter | Column 2 Types of Non-Event Process Effluent Streams | Column 3 Monitoring Frequency | Column 4 Daily Concentration Limit mg/L | Column 5 Monthly Average Concentration Limit mg/L |
| --- | --- | --- | --- | --- | --- | --- |
| 1. | 8 | Total Suspended Solids | ATWE | Daily | 70.0 | 25.0 |
| 2. | 8 | Total Suspended Solids | WTPE | Daily | 70.0 | 25.0 |
| 3. | 9 | Aluminum | ATWE | Weekly | 13.0 | 4.50 |
| 4. | 9 | Aluminum | WTPE | Weekly | 13.0 | 4.50 |
| 5. | 9a | Iron | ATWE | Weekly | 2.50 | 1.0 |
| 6. | 9a | Iron | WTPE | Weekly | 2.50 | 1.0 |
| 7. | 25 | Oil and grease | OWSE | Weekly | 29.0 | 13.0 |

Explanatory Notes:

Types of Non-Event Process Effluent Streams in Column 2:

ATWE = a stream of the type described in paragraph 3 of subsection 1 (2)

WTPE = a stream of the type described in paragraph 1 of subsection 1 (2)

OWSE = a stream of the type described in paragraph 6 of subsection 1 (2)

Table 2
Plant: Bruce Bulk Steam System

| Item | Analytical Test Group | Column 1 Parameter | Column 2 Types of Non-Event Process Effluent Streams | Column 3 Monitoring Frequency | Column 4 Daily Concentration Limit mg/L | Column 5 Monthly Average Concentration Limit mg/L |
| --- | --- | --- | --- | --- | --- | --- |
| 1. | 8 | Total Suspended Solids | WTPE | Daily | 70.0 | 25.0 |
| 2. | 9 | Aluminum | WTPE | Weekly | 13.0 | 4.50 |
| 3. | 9a | Iron | WTPE | Weekly | 2.50 | 1.0 |

Explanatory Note:

Types of Non-Event Process Effluent Streams in Column 2:

WTPE = a stream of the type described in paragraph 1 of subsection 1 (2)

Table 3
PLANT: Bruce Heavy Water Plant

| Item | Analytical Test Group | Column 1 Parameter | Column 2 Types of Non-Event Process Effluent Streams | Column 3 Monitoring Frequency | Column 4 Daily Concentration Limit mg/L | Column 5 Monthly Average Concentration Limit mg/L |
| --- | --- | --- | --- | --- | --- | --- |
| 1. | 15 | Sulphide | EUSPE | Daily | 0.8 | Not applicable |

Explanatory Note:

Types of Non-Event Process Effluent Streams in Column 2:

EUSPE = a stream of the type described in paragraph 7 of subsection 1 (2)

Table 4
PLANT: Bruce NGS — A

| Item | Analytical Test Group | Column 1 Parameter | Column 2 Types of Non-Event Process Effluent Streams | Column 3 Monitoring Frequency | Column 4 Daily Concentration Limit mg/L | Column 5 Monthly Average Concentration Limit mg/L |
| --- | --- | --- | --- | --- | --- | --- |
| 1. | 8 | Total Suspended Solids | WTPE | Daily | 70.0 | 25.0 |
| 2. | 9 | Aluminum | WTPE | Weekly | 13.0 | 4.50 |
| 3. | 9a | Iron | WTPE | Weekly | 2.50 | 1.0 |

Explanatory Note:

Types of Non-Event Process Effluent Streams in Column 2:

WTPE = a stream of the type described in paragraph 1 of subsection 1 (2)

Table 5
PLANT: Bruce NGS — B

| Item | Analytical Test Group | Column 1 Parameter | Column 2 Types of Non-Event Process Effluent Streams | Column 3 Monitoring Frequency | Column 4 Daily Concentration Limit mg/L | Column 5 Monthly Average Concentration Limit mg/L |
| --- | --- | --- | --- | --- | --- | --- |
| 1. | 8 | Total Suspended Solids | WTPE | Daily | 70.0 | 25.0 |
| 2. | 9 | Aluminum | WTPE | Weekly | 13.0 | 4.50 |
| 3. | 9a | Iron | WTPE | Weekly | 2.50 | 1.0 |

Explanatory Note:

Types of Non-Event Process Effluent Streams in Column 2:

WTPE = a stream of the type described in paragraph 1 of subsection 1 (2)

Table 6
PLANT: Bruce Nuclear Power Development

| Item | Analytical Test Group | Column 1 Parameter | Column 2 Types of Non-Event Process Effluent Streams | Column 3 Monitoring Frequency | Column 4 Daily Concentration Limit mg/L | Column 5 Monthly Average Concentration Limit mg/L |
| --- | --- | --- | --- | --- | --- | --- |
| 1. | 1a | Biochemical Oxygen Demand (5 Day) | ISTPE | Weekly | Not applicable | 25.0 |
| 2. | 4a | Ammonia plus Ammonium | ISTPE | Weekly | Not applicable | 7.0 |
| 3. | 6 | Total Phosphorus | ISTPE | Weekly | Not applicable | 1.0 |
| 4. | 8 | Total Suspended Solids | ISTPE | Daily | 44.0 | 18.0 |
| 5. | 25 | Oil and grease | ISTPE | Weekly | 38.0 | 12.0 |

Explanatory Note:

Types of Non-Event Process Effluent Streams in Column 2:

ISTPE = a stream of the type described in paragraph 2 of subsection 1 (2)

Table 7
PLANT: Darlington NGS

| Item | Analytical Test Group | Column 1 Parameter | Column 2 Types of Non-Event Process Effluent Streams | Column 3 Monitoring Frequency | Column 4 Daily Concentration Limit mg/L | Column 5 Monthly Average Concentration Limit mg/L |
| --- | --- | --- | --- | --- | --- | --- |
| 1. | 1a | Biochemical Oxygen Demand (5 Day) | ISTPE | Weekly | Not applicable | 25.0 |
| 2. | 4a | Ammonia plus Ammonium | ISTPE | Weekly | Not applicable | 7.0 |
| 3. | 6 | Total Phosphorus | ISTPE | Weekly | Not applicable | 4.60 |
| 4. | 8 | Total Suspended Solids | ISTPE | Daily | 44.0 | 18.0 |
| 5. | 8 | Total Suspended Solids | WTPE | Daily | 70.0 | 25.0 |
| 6. | 9 | Aluminum | WTPE | Weekly | 13.0 | 4.50 |
| 7. | 9a | Iron | WTPE | Weekly | 2.50 | 1.0 |
| 8. | 25 | Oil and grease | ISTPE | Weekly | 38.0 | 12.0 |

Explanatory Notes:

Types of Non-Event Process Effluent Streams in Column 2:

WTPE = a stream of the type described in paragraph 1 of subsection 1 (2)

ISTPE = a stream of the type described in paragraph 2 of subsection 1 (2)

Table 8
Plant: J.C. Keith TGS

| Item | Analytical Test Group | Column 1 Parameter | Column 2 Types of Non-Event Process Effluent Streams | Column 3 Monitoring Frequency | Column 4 Daily Concentration Limit mg/L | Column 5 Monthly Average Concentration Limit mg/L |
| --- | --- | --- | --- | --- | --- | --- |
| 1. | 8 | Total Suspended Solids | ATWE | Daily | 70.0 | 25.0 |
| 2. | 8 | Total Suspended Solids | WTPE | Daily | 70.0 | 25.0 |
| 3. | 9 | Aluminum | ATWE | Weekly | 13.0 | 4.50 |
| 4. | 9 | Aluminum | WTPE | Weekly | 13.0 | 4.50 |
| 5. | 9a | Iron | ATWE | Weekly | 2.50 | 1.0 |
| 6. | 9a | Iron | WTPE | Weekly | 2.50 | 1.0 |
| 7. | 25 | Oil and grease | OWSE | Weekly | 29.0 | 13.0 |

Explanatory Notes:

Types of Non-Event Process Effluent Streams in Column 2:

ATWE = a stream of the type described in paragraph 3 of subsection 1 (2)

WTPE = a stream of the type described in paragraph 1 of subsection 1 (2)

OWSE = a stream of the type described in paragraph 6 of subsection 1 (2)

Table 9
PLANT: Lakeview TGS

| Item | Analytical Test Group | Column 1 Parameter | Column 2 Types of Non-Event Process Effluent Streams | Column 3 Monitoring Frequency | Column 4 Daily Concentration Limit mg/L | Column 5 Monthly Average Concentration Limit mg/L |
| --- | --- | --- | --- | --- | --- | --- |
| 1. | 8 | Total Suspended Solids | ATWE | Daily | 70.0 | 25.0 |
| 2. | 8 | Total Suspended Solids | BSWE | Daily | 70.0 | 25.0 |
| 3. | 8 | Total Suspended Solids | AQWE | Daily | 70.0 | 25.0 |
| 4. | 9 | Aluminum | ATWE | Weekly | 13.0 | 4.50 |
| 5. | 9 | Aluminum | BSWE | Weekly | 13.0 | 4.50 |
| 6. | 9 | Aluminum | AQWE | Weekly | 13.0 | 4.50 |
| 7. | 9a | Iron | ATWE | Weekly | 2.50 | 1.0 |
| 8. | 9a | Iron | BSWE | Weekly | 2.50 | 1.0 |
| 9. | 9a | Iron | AQWE | Weekly | 2.50 | 1.0 |
| 10. | 25 | Oil and grease | OWSE | Weekly | 29.0 | 13.0 |

Explanatory Notes:

Types of Non-Event Process Effluent Streams in Column 2:

ATWE = a stream of the type described in paragraph 3 of subsection 1 (2)

BSWE = a stream of the type described in paragraph 5 of subsection 1 (2)

AQWE = a stream of the type described in paragraph 4 of subsection 1 (2)

OWSE = a stream of the type described in paragraph 6 of subsection 1 (2)

Table 10
PLANT: Lambton TGS

| Item | Analytical Test Group | Column 1 Parameter | Column 2 Types of Non-Event Process Effluent Streams | Column 3 Monitoring Frequency | Column 4 Daily Concentration Limit mg/L | Column 5 Monthly Average Concentration Limit mg/L |
| --- | --- | --- | --- | --- | --- | --- |
| 1. | 8 | Total Suspended Solids | ATWE | Daily | 70.0 | 25.0 |
| 2. | 8 | Total Suspended Solids | BSWE | Daily | 70.0 | 25.0 |
| 3. | 8 | Total Suspended Solids | AQWE | Daily | 70.0 | 25.0 |
| 4. | 9 | Aluminum | ATWE | Weekly | 13.0 | 4.50 |
| 5. | 9 | Aluminum | BSWE | Weekly | 13.0 | 4.50 |
| 6. | 9 | Aluminum | AQWE | Weekly | 13.0 | 4.50 |
| 7. | 9a | Iron | ATWE | Weekly | 2.50 | 1.0 |
| 8. | 9a | Iron | BSWE | Weekly | 2.50 | 1.0 |
| 9. | 9a | Iron | AQWE | Weekly | 2.50 | 1.0 |

Explanatory Notes:

Types of Non-Event Process Effluent Streams in Column 2:

ATWE = a stream of the type described in paragraph 3 of subsection 1 (2)

BSWE = a stream of the type described in paragraph 5 of subsection 1 (2)

AQWE = a stream of the type described in paragraph 4 of subsection 1 (2)

Table 11
PLANT: Lennox TGS

| Item | Analytical Test Group | Column 1 Parameter | Column 2 Types of Non-Event Process Effluent Streams | Column 3 Monitoring Frequency | Column 4 Daily Concentration Limit mg/L | Column 5 Monthly Average Concentration Limit mg/L |
| --- | --- | --- | --- | --- | --- | --- |
| 1. | 8 | Total Suspended Solids | WTPE | Daily | 70.0 | 25.0 |
| 2. | 9 | Aluminum | WTPE | Weekly | 13.0 | 4.50 |
| 3. | 9a | Iron | WTPE | Weekly | 2.50 | 1.0 |
| 4. | 25 | Oil and grease | OWSE | Weekly | 29.0 | 13.0 |

Explanatory Notes:

Types of Non-Event Process Effluent Streams in Column 2:

WTPE = a stream of the type described in paragraph 1 of subsection 1 (2)

OWSE = a stream of the type described in paragraph 6 of subsection 1 (2)

Table 12
PLANT: Nanticoke TGS

| Item | Analytical Test Group | Column 1 Parameter | Column 2 Types of Non-Event Process Effluent Streams | Column 3 Monitoring Frequency | Column 4 Daily Concentration Limit mg/L | Column 5 Monthly Average Concentration Limit mg/L |
| --- | --- | --- | --- | --- | --- | --- |
| 1. | 8 | Total Suspended Solids | ATWE | Daily | 70.0 | 25.0 |
| 2. | 8 | Total Suspended Solids | BSWE | Daily | 70.0 | 25.0 |
| 3. | 8 | Total Suspended Solids | AQWE | Daily | 70.0 | 25.0 |
| 4. | 8 | Total Suspended Solids | ATLE | Daily | 70.0 | 25.0 |
| 5. | 9 | Aluminum | ATWE | Weekly | 13.0 | 4.50 |
| 6. | 9 | Aluminum | BSWE | Weekly | 13.0 | 4.50 |
| 7. | 9 | Aluminum | AQWE | Weekly | 13.0 | 4.50 |
| 8. | 9 | Aluminum | ATLE | Weekly | 13.0 | 4.50 |
| 9. | 9a | Iron | ATWE | Weekly | 2.50 | 1.0 |
| 10. | 9a | Iron | BSWE | Weekly | 2.50 | 1.0 |
| 11. | 9a | Iron | AQWE | Weekly | 2.50 | 1.0 |
| 12. | 9a | Iron | ATLE | Weekly | 2.50 | 1.0 |

Explanatory Notes:

Types of Non-Event Process Effluent Streams in Column 2:

ATWE = a stream of the type described in paragraph 3 of subsection 1 (2)

BSWE = a stream of the type described in paragraph 5 of subsection 1 (2)

AQWE = a stream of the type described in paragraph 4 of subsection 1 (2)

ATLE = a stream of the type described in paragraph 8 of subsection 1 (2)

Table 13
PLANT: Pickering NGS — A and B

| Item | Analytical Test Group | Column 1 Parameter | Column 2 Types of Non-Event Process Effluent Streams | Column 3 Monitoring Frequency | Column 4 Daily Concentration Limit mg/L | Column 5 Monthly Average Concentration Limit mg/L |
| --- | --- | --- | --- | --- | --- | --- |
| 1. | 8 | Total Suspended Solids | WTPE | Daily | 70.0 | 25.0 |
| 2. | 9 | Aluminum | WTPE | Weekly | 13.0 | 4.50 |
| 3. | 9a | Iron | WTPE | Weekly | 2.50 | 1.0 |

Explanatory Note:

Types of Non-Event Process Effluent Streams in Column 2:

WTPE = a stream of the type described in paragraph 1 of subsection 1 (2)

Table 14
PLANT: R.L. Hearn TGS

| Item | Analytical Test Group | Column 1 Parameter | Column 2 Types of Non-Event Process Effluent Streams | Column 3 Monitoring Frequency | Column 4 Daily Concentration Limit mg/L | Column 5 Monthly Average Concentration Limit mg/L |
| --- | --- | --- | --- | --- | --- | --- |
| 1. | 8 | Total Suspended Solids | ATWE | Daily | 70.0 | 25.0 |
| 2. | 8 | Total Suspended Solids | WTPE | Daily | 70.0 | 25.0 |
| 3. | 9 | Aluminum | ATWE | Weekly | 13.0 | 4.50 |
| 4. | 9 | Aluminum | WTPE | Weekly | 13.0 | 4.50 |
| 5. | 9a | Iron | ATWE | Weekly | 2.50 | 1.0 |
| 6. | 9a | Iron | WTPE | Weekly | 2.50 | 1.0 |
| 7. | 25 | Oil and grease | OWSE | Weekly | 29.0 | 13.0 |

Explanatory Notes:

Types of Non-Event Process Effluent Streams in Column 2:

ATWE = a stream of the type described in paragraph 3 of subsection 1 (2)

WTPE = a stream of the type described in paragraph 1 of subsection 1 (2)

OWSE = a stream of the type described in paragraph 6 of subsection 1 (2)

Table 15
PLANT: Thunder Bay TGS

| Item | Analytical Test Group | Column 1 Parameter | Column 2 Types of Non-Event Process Effluent Streams | Column 3 Monitoring Frequency | Column 4 Daily Concentration Limit mg/L | Column 5 Monthly Average Concentration Limit mg/L |
| --- | --- | --- | --- | --- | --- | --- |
| 1. | 8 | Total Suspended Solids | ATWE | Daily | 70.0 | 25.0 |
| 2. | 8 | Total Suspended Solids | WTPE | Daily | 70.0 | 25.0 |
| 3. | 9 | Aluminum | ATWE | Weekly | 13.0 | 4.50 |
| 4. | 9 | Aluminum | WTPE | Weekly | 13.0 | 4.50 |
| 5. | 9a | Iron | ATWE | Weekly | 2.50 | 1.0 |
| 6. | 9a | Iron | WTPE | Weekly | 2.50 | 1.0 |
| 7. | 25 | Oil and grease | OWSE | Weekly | 29.0 | 13.0 |

Explanatory Notes:

Types of Non-Event Process Effluent Streams in Column 2:

ATWE = a stream of the type described in paragraph 3 of subsection 1 (2)

WTPE = a stream of the type described in paragraph 1 of subsection 1 (2)

OWSE = a stream of the type described in paragraph 6 of subsection 1 (2)

Schedule 3
Types of Event Process Effluent Streams, Limits, Monitoring Frequency

Table 1
PLANT: Atikokan TGS

| Item | Analytical Test Group | Column 1 Parameter | Column 2 Types of Event Process Effluent Streams | Column 3 Monitoring Frequency | Column 4 Daily Concentration Limit mg/L | Column 5 Monthly Average Concentration Limit mg/L |
| --- | --- | --- | --- | --- | --- | --- |
| 1. | 8 | Total Suspended Solids | CSSE | Daily | 25.0 | Not applicable |
| 2. | 8 | Total Suspended Solids | ECE | Daily | 25.0 | Not applicable |
| 3. | 9a | Iron | CSSE | Daily | 1.0 | Not applicable |
| 4. | 9a | Iron | ECE | Daily | 1.0 | Not applicable |

Explanatory Notes:

Types of Event Process Effluent Streams in Column 2:

CSSE = a stream of the type described in paragraph 1 of subsection 1 (3)

ECE = a stream of the type described in paragraph 3 of subsection 1 (3)

Table 2
PLANT: Bruce Bulk Steam System

| Item | Analytical Test Group | Column 1 Parameter | Column 2 Types of Event Process Effluent Streams | Column 3 Monitoring Frequency | Column 4 Daily Concentration Limit mg/L | Column 5 Monthly Average Concentration Limit mg/L |
| --- | --- | --- | --- | --- | --- | --- |
| 1. | 8 | Total Suspended Solids | ECE | Daily | 25.0 | Not applicable |
| 2. | 9a | Iron | ECE | Daily | 1.0 | Not applicable |

Explanatory Note:

Types of Event Process Effluent Streams in Column 2:

ECE = a stream of the type described in paragraph 3 of subsection 1 (3)

Table 3
PLANT: Bruce Heavy Water Plant

| Item | Analytical Test Group | Column 1 Parameter | Column 2 Types of Event Process Effluent Streams | Column 3 Monitoring Frequency | Column 4 Daily Concentration Limit mg/L | Column 5 Monthly Average Concentration Limit mg/L |
| --- | --- | --- | --- | --- | --- | --- |
| 1. | 8 | Total Suspended Solids | ECE | Daily | 25.0 | Not applicable |
| 2. | 9a | Iron | ECE | Daily | 1.0 | Not applicable |
| 3. | 15 | Sulphide | HLE | Daily | 0.8 | Not applicable |

Explanatory Notes:

Types of Event Process Effluent Streams in Column 2:

ECE = a stream of the type described in paragraph 3 of subsection 1 (3)

HLE = a stream of the type described in paragraph 5 of subsection 1 (3)

Table 4
PLANT: Bruce NGS — A

| Item | Analytical Test Group | Column 1 Parameter | Column 2 Types of Event Process Effluent Streams | Column 3 Monitoring Frequency | Column 4 Daily Concentration Limit mg/L | Column 5 Monthly Average Concentration Limit mg/L |
| --- | --- | --- | --- | --- | --- | --- |
| 1. | 6 | Total Phosphorus | RLWMSTE | Weekly | Not applicable | 1.0 |
| 2. | 8 | Total Suspended Solids | ECE | Daily | 25.0 | Not applicable |
| 3. | 8 | Total Suspended Solids | RLWMSTE | Daily | 73.0 | 21.0 |
| 4. | 9 | Zinc | RLWMSTE | Weekly | 1.0 | 0.50 |
| 5. | 9a | Iron | ECE | Daily | 1.0 | Not applicable |
| 6. | 9a | Iron | RLWMSTE | Weekly | 9.0 | 3.0 |
| 7. | 25 | Oil and grease | RLWMSTE | Weekly | 36.0 | 13.0 |

Explanatory Notes:

Types of Event Process Effluent Streams in Column 2:

RLWMSTE = a stream of the type described in paragraph 2 of subsection 1 (3)

ECE = a stream of the type described in paragraph 3 of subsection 1 (3)

Table 5
PLANT: Bruce NGS — B

| Item | Analytical Test Group | Column 1 Parameter | Column 2 Types of Event Process Effluent Streams | Column 3 Monitoring Frequency | Column 4 Daily Concentration Limit mg/L | Column 5 Monthly Average Concentration Limit mg/L |
| --- | --- | --- | --- | --- | --- | --- |
| 1. | 6 | Total Phosphorus | RLWMSTE | Weekly | Not applicable | 1.0 |
| 2. | 8 | Total Suspended Solids | ECE | Daily | 25.0 | Not applicable |
| 3. | 8 | Total Suspended Solids | RLWMSTE | Daily | 73.0 | 21.0 |
| 4. | 9 | Zinc | RLWMSTE | Weekly | 1.0 | 0.50 |
| 5. | 9a | Iron | ECE | Daily | 1.0 | Not applicable |
| 6. | 9a | Iron | RLWMSTE | Weekly | 9.0 | 3.0 |
| 7. | 25 | Oil and grease | RLWMSTE | Weekly | 36.0 | 13.0 |

Explanatory Notes:

Types of Event Process Effluent Streams in Column 2:

RLWMSTE = a stream of the type described in paragraph 2 of subsection 1 (3)

ECE = a stream of the type described in paragraph 3 of subsection 1 (3)

Table 6
PLANT: Bruce Nuclear Power Development

| Item | Analytical Test Group | Column 1 Parameter | Column 2 Types of Event Process Effluent Streams | Column 3 Monitoring Frequency | Column 4 Daily Concentration Limit mg/L | Column 5 Monthly Average Concentration Limit mg/L |
| --- | --- | --- | --- | --- | --- | --- |
| 1. | 8 | Total Suspended Solids | ECE | Daily | 25.0 | Not applicable |
| 2. | 9a | Iron | ECE | Daily | 1.0 | Not applicable |

Explanatory Notes:

Types of Event Process Effluent Streams in Column 2:

ECE = a stream of the type described in paragraph 3 of subsection 1 (3)

Table 7
PLANT: Darlington NGS

| Item | Analytical Test Group | Column 1 Parameter | Column 2 Types of Event Process Effluent Streams | Column 3 Monitoring Frequency | Column 4 Daily Concentration Limit mg/L | Column 5 Monthly Average Concentration Limit mg/L |
| --- | --- | --- | --- | --- | --- | --- |
| 1. | 6 | Total Phosphorus | RLWMSTE | Weekly | Not applicable | 1.0 |
| 2. | 8 | Total Suspended Solids | ECE | Daily | 25.0 | Not applicable |
| 3. | 8 | Total Suspended Solids | RLWMSTE | Daily | 73.0 | 21.0 |
| 4. | 9 | Zinc | RLWMSTE | Weekly | 1.0 | 0.50 |
| 5. | 9a | Iron | ECE | Daily | 1.0 | Not applicable |
| 6. | 9a | Iron | RLWMSTE | Weekly | 9.0 | 3.0 |
| 7. | 25 | Oil and grease | RLWMSTE | Weekly | 36.0 | 13.0 |
| 8. | 25 | Oil and grease | OWSE | Daily | 15.0 | Not applicable |

Explanatory Notes:

Types of Event Process Effluent Streams in Column 2:

ECE = a stream of the type described in paragraph 3 of subsection 1 (3)

RLWMSTE = a stream of the type described in paragraph 2 of subsection 1 (3)

OWSE = a stream of the type described in paragraph 4 of subsection 1 (3)

Table 8
PLANT: J.C. Keith TGS

| Item | Analytical Test Group | Column 1 Parameter | Column 2 Types of Event Process Effluent Streams | Column 3 Monitoring Frequency | Column 4 Daily Concentration Limit mg/L | Column 5 Monthly Average Concentration Limit mg/L |
| --- | --- | --- | --- | --- | --- | --- |
| 1. | 8 | Total Suspended Solids | ECE | Daily | 25.0 | Not applicable |
| 2. | 9a | Iron | ECE | Daily | 1.0 | Not applicable |

Explanatory Note:

Types of Event Process Effluent Streams in Column 2:

ECE = a stream of the type described in paragraph 3 of subsection 1 (3)

Table 9
PLANT: Lakeview TGS

| Item | Analytical Test Group | Column 1 Parameter | Column 2 Types of Event Process Effluent Streams | Column 3 Monitoring Frequency | Column 4 Daily Concentration Limit mg/L | Column 5 Monthly Average Concentration Limit mg/L |
| --- | --- | --- | --- | --- | --- | --- |
| 1. | 8 | Total Suspended Solids | CSSE | Daily | 25.0 | Not applicable |
| 2. | 8 | Total Suspended Solids | ECE | Daily | 25.0 | Not applicable |
| 3. | 9a | Iron | CSSE | Daily | 1.0 | Not applicable |
| 4. | 9a | Iron | ECE | Daily | 1.0 | Not applicable |

Explanatory Notes:

Types of Event Process Effluent Streams in Column 2:

CSSE = a stream of the type described in paragraph 1 of subsection 1 (3)

ECE = a stream of the type described in paragraph 3 of subsection 1 (3)

Table 10
PLANT: Lambton TGS

| Item | Analytical Test Group | Column 1 Parameter | Column 2 Types of Event Process Effluent Streams | Column 3 Monitoring Frequency | Column 4 Daily Concentration Limit mg/L | Column 5 Monthly Average Concentration Limit mg/L |
| --- | --- | --- | --- | --- | --- | --- |
| 1. | 8 | Total Suspended Solids | ECE | Daily | 25.0 | Not applicable |
| 2. | 8 | Total Suspended Solids | CSSE | Weekly | 70.0 | 25.0 |
| 3. | 9 | Aluminum | CSSE | Weekly | 13.0 | 4.50 |
| 4. | 9a | Iron | ECE | Daily | 1.0 | Not applicable |
| 5. | 9a | Iron | CSSE | Weekly | 2.50 | 1.0 |

Explanatory Notes:

Types of Event Process Effluent Streams in Column 2:

CSSE = a stream of the type described in paragraph 1 of subsection 1 (3)

ECE = a stream of the type described in paragraph 3 of subsection 1 (3)

Table 11
PLANT: Lennox TGS

| Item | Analytical Test Group | Column 1 Parameter | Column 2 Types of Event Process Effluent Streams | Column 3 Monitoring Frequency | Column 4 Daily Concentration Limit mg/L | Column 5 Monthly Average Concentration Limit mg/L |
| --- | --- | --- | --- | --- | --- | --- |
| 1. | 8 | Total Suspended Solids | ECE | Daily | 25.0 | Not applicable |
| 2. | 9a | Iron | ECE | Daily | 1.0 | Not applicable |

Explanatory Note:

Types of Event Process Effluent Streams in Column 2:

ECE = a stream of the type described in paragraph 3 of subsection 1 (3)

Table 12
PLANT: Nanticoke TGS

| Item | Analytical Test Group | Column 1 Parameter | Column 2 Types of Event Process Effluent Streams | Column 3 Monitoring Frequency | Column 4 Daily Concentration Limit mg/L | Column 5 Monthly Average Concentration Limit mg/L |
| --- | --- | --- | --- | --- | --- | --- |
| 1. | 8 | Total Suspended Solids | ECE | Daily | 25.0 | Not applicable |
| 2. | 9a | Iron | ECE | Daily | 1.0 | Not applicable |

Explanatory Note:

Types of Event Process Effluent Streams in Column 2:

ECE = a stream of the type described in paragraph 3 of subsection 1 (3)

Table 13
PLANT: Pickering NGS — A and B

| Item | Analytical Test Group | Column 1 Parameter | Column 2 Types of Event Process Effluent Streams | Column 3 Monitoring Frequency | Column 4 Daily Concentration Limit mg/L | Column 5 Monthly Average Concentration Limit mg/L |
| --- | --- | --- | --- | --- | --- | --- |
| 1. | 6 | Total Phosphorus | RLWMSTE | Weekly | Not applicable | 1.0 |
| 2. | 8 | Total Suspended Solids | ECE | Daily | 25.0 | Not applicable |
| 3. | 8 | Total Suspended Solids | RLWMSTE | Daily | 73.0 | 21.0 |
| 4. | 9 | Zinc | RLWMSTE | Weekly | 1.0 | 0.50 |
| 5. | 9a | Iron | ECE | Daily | 1.0 | Not applicable |
| 6. | 9a | Iron | RLWMSTE | Weekly | 9.0 | 3.0 |
| 7. | 25 | Oil and grease | RLWMSTE | Weekly | 36.0 | 13.0 |
| 8. | 25 | Oil and grease | OWSE | Daily | 15.0 | Not applicable |

Explanatory Notes:

Types of Event Process Effluent Streams in Column 2:

RLWMSTE = a stream of the type described in paragraph 2 of subsection 1 (3)

ECE = a stream of the type described in paragraph 3 of subsection 1 (3)

OWSE = a stream of the type described in paragraph 4 of subsection 1 (3)

Table 14
PLANT: R. L. Hearn TGS

| Item | Analytical Test Group | Column 1 Parameter | Column 2 Types of Event Process Effluent Streams | Column 3 Monitoring Frequency | Column 4 Daily Concentration Limit mg/L | Column 5 Monthly Average Concentration Limit mg/L |
| --- | --- | --- | --- | --- | --- | --- |
| 1. | 8 | Total Suspended Solids | ECE | Daily | 25.0 | Not applicable |
| 2. | 9a | Iron | ECE | Daily | 25.0 | Not applicable |

Explanatory Note:

Types of Event Process Effluent Streams in Column 2:

ECE = a stream of the type described in paragraph 3 of subsection 1 (3)

Table 15
PLANT: Thunder Bay TGS

| Item | Analytical Test Group | Column 1 Parameter | Column 2 Types of Event Process Effluent Streams | Column 3 Monitoring Frequency | Column 4 Daily Concentration Limit mg/L | Column 5 Monthly Average Concentration Limit mg/L |
| --- | --- | --- | --- | --- | --- | --- |
| 1. | 8 | Total Suspended Solids | ECE | Daily | 25.0 | Not applicable |
| 2. | 9a | Iron | ECE | Daily | 1.0 | Not applicable |

Explanatory Note:

Types of Event Process Effluent Streams in Column 2:

ECE = a stream of the type described in paragraph 3 of subsection 1 (3)

Commencement

8.  This Regulation comes into force on the day it is filed.

Back to top

Back to top