ontario regulation 318/17

made under the

Green Energy Act, 2009

Made: July 26, 2017
Filed: August 1, 2017
Published on e-Laws: August 1, 2017
Printed in The Ontario Gazette: August 19, 2017

Amending O. Reg. 404/12

(ENERGY and water EFFICIENCY - APPLIANCES AND PRODUCTS)

1.  Subsection 2 (3) of Ontario Regulation 404/12 is revoked and the following substituted:

(3)  Symbols and acronyms used in the Schedules have the following meanings, unless the context requires otherwise:

1.	AC: alternating current.

2.	AFUE: annual fuel utilization efficiency.

3.	AHRI: Air-Conditioning, Heating and Refrigeration Institute.

4.	ANSI: American National Standards Institute.

5.	BIL: basic impulse insulation level.

6.	Btu/h: British thermal units per hour.

7.	CGA: Canadian Gas Association.

8.	CIE: International Commission on Illumination.

9.	COP: coefficient of performance.

10.	CSA: Canadian Standards Association.

11.	C: degree(s) Celsius.

12.	DC: direct current.

13.	EER: energy efficiency ratio.

14.	Federal Energy Efficiency Regulations (May 4, 2012 version): SOR/94-651 (Energy Efficiency Regulations) made under the Energy Efficiency Act (Canada) as the Regulations read on May 4, 2012.

15.	HSPF V: heating season performance factors — region V.

16.	Hz: hertz.

17.	IEC: International Electrotechnical Commission.

18.	IEER: integrated energy efficiency ratio.

19.	IES: Illuminating Engineering Society of North America.

20.	kV: kilovolts.

21.	kVA: kilovolt-amperes.

22.	kW: kilowatts.

23.	kWh: kilowatt-hours.

24.	L: litres.

25.	lm/W: lumens per watt.

26.	mL/s: millilitres per second.

27.	NEMA: National Electrical Manufacturers Association.

28.	NFRC: National Fenestration Rating Council.

29.	SDHV: small duct high velocity.

30.	U.S. DOE: United States Department of Energy.

31.	VRF: variable refrigerant flow.

32.	W: watts.

33.	W/(m²C): watts per meter squared degrees Celsius.

2.  Table 1 of the Regulation is revoked.

3.  Subparagraph 18 i of section 1 of Schedule 1 to the Regulation is amended by striking out “June 5, 2017” and substituting “January 1, 2020”.

4.  (1)  Sub-subparagraph 2 i A of section 1 of Schedule 4 to the Regulation is revoked and the following substituted:

A.	For an air conditioner or heat pump with at least 19 kW (65,000 Btu/h) of cooling capacity, excluding packaged terminal and single-package vertical air conditioners and heat pumps, the day before the earliest applicable compliance date for the particular air conditioner or heat pump as set out in Column 7 of Table 1 and Column 9 of Tables 2 and 3 to sub-subparagraph 2.1 iv A.  For greater certainty, the particular air conditioner or heat pump is described in Columns 2, 3 and 4, read together, of Tables 1, 2 and 3.

(2)  Sub-subparagraph 2.1 i A of section 1 of Schedule 4 to the Regulation is revoked and the following substituted:

A.	For an air conditioner or heat pump described in the Tables to sub-subparagraph iv A, from the later applicable compliance date for the particular air conditioner or heat pump as set out in Column 7 of Table 1 and Column 9 of Tables 2 and 3 to December 31, 2017, inclusive. For greater certainty, the particular air conditioner or heat pump is described in Columns 2, 3 and 4, read together, of Tables 1, 2 and 3.

(3)  Sub-subparagraph 2.1 iv A of section 1 of Schedule 4 to the Regulation is amended by striking out “Table” and substituting “Tables”.

(4)  The Table to sub-subparagraph 2.1 iv A of section 1 of Schedule 4 to the Regulation is revoked and the following substituted:

table 1
Large unitary air conditioners

| Column 1 Item | Column 2 Sub-type | Column 3 Heating type | Column 4 Cooling capacity | Column 5 EER | Column 6 IEER | Column 7 Compliance date |
| --- | --- | --- | --- | --- | --- | --- |
| 1. | Air-cooled | A | ≥19 kW and <40 kW | 11.2 | 11.4 | January 1, 2013 |
| 2. | Air-cooled | A | ≥40 kW and <70 kW | 11.0 | 11.2 | January 1, 2013 |
| 3. | Air-cooled | A | ≥70 kW and <223 kW | 10.0 | 10.1 | January 1, 2013 |
| 4. | Air-cooled | A | ≥223 kW | 9.7 | 9.8 | January 1, 2013 |
| 5. | Air-cooled | B | ≥19 kW and <40 kW | 11.0 | 11.2 | January 1, 2013 |
| 6. | Air-cooled | B | ≥40 kW and <70 kW | 10.8 | 11.0 | January 1, 2013 |
| 7. | Air-cooled | B | ≥70 kW and <223 kW | 9.8 | 9.9 | January 1, 2013 |
| 8. | Air-cooled | B | ≥223 kW | 9.5 | 9.6 | January 1, 2013 |
| 9. | Water-cooled, other than VRF multi-split | A | ≥19 kW and <40 kW | 12.1 | 11.7 | July 1, 2013 |
| 10. | Water-cooled, other than VRF multi-split | A | ≥40 kW and <70 kW | 11.0 | 11.2 | January 1, 2013 |
| 11. | Water-cooled, other than VRF multi-split | A | ≥40 kW and <70 kW | 12.5 | 11.2 | July 1, 2014 |
| 12. | Water-cooled, other than VRF multi-split | A | ≥70 kW and <223 kW | 11.0 | 11.1 | January 1, 2013 |
| 13. | Water-cooled, other than VRF multi-split | A | ≥70 kW and <223 kW | 12.4 | 11.1 | July 1, 2014 |
| 14. | Water-cooled, other than VRF multi-split | A | ≥223 kW | 11.0 | 11.1 | January 1, 2013 |
| 15. | Water-cooled, other than VRF multi-split | B | ≥19 kW and <40 kW | 11.9 | 11.5 | July 1, 2013 |
| 16. | Water-cooled, other than VRF multi-split | B | ≥40 kW and <70 kW | 11.0 | 11.0 | July 1, 2013 |
| 17. | Water-cooled, other than VRF multi-split | B | ≥40 kW and <70 kW | 12.3 | 11.0 | July 1, 2014 |
| 18. | Water-cooled, other than VRF multi-split | B | ≥70 kW and <223 kW | 10.8 | 10.9 | January 1, 2013 |
| 19. | Water-cooled, other than VRF multi-split | B | ≥70 kW and <223 kW | 12.2 | 10.9 | July 1, 2014 |
| 20. | Water-cooled, other than VRF multi-split | B | ≥223 kW | 10.8 | 10.9 | January 1, 2013 |
| 21. | Evaporation-cooled, other than VRF multi-split | A | ≥19 kW and <40 kW | 12.1 | 11.7 | July 1, 2013 |
| 22. | Evaporation-cooled, other than VRF multi-split | A | ≥40 kW and <70 kW | 11.0 | 11.2 | January 1, 2013 |
| 23. | Evaporation-cooled, other than VRF multi-split | A | ≥40 kW and <70 kW | 12.0 | 11.2 | July 1, 2014 |
| 24. | Evaporation-cooled, other than VRF multi-split | A | ≥70 kW and <223 kW | 11.0 | 11.1 | January 1, 2013 |
| 25. | Evaporation-cooled, other than VRF multi-split | A | ≥70 kW and <223 kW | 11.9 | 11.1 | July 1, 2014 |
| 26. | Evaporation-cooled, other than VRF multi-split | A | ≥223 kW | 11.0 | 11.1 | January 1, 2013 |
| 27. | Evaporation-cooled, other than VRF multi-split | B | ≥19 kW and <40 kW | 11.9 | 11.5 | July 1, 2013 |
| 28. | Evaporation-cooled, other than VRF multi-split | B | ≥40 kW and <70 kW | 11.0 | 11.0 | July 1, 2013 |
| 29. | Evaporation-cooled, other than VRF multi-split | B | ≥40 kW and <70 kW | 11.8 | 11.0 | July 1, 2014 |
| 30. | Evaporation-cooled, other than VRF multi-split | B | ≥70 kW and <223 kW | 10.8 | 10.9 | January 1, 2013 |
| 31. | Evaporation-cooled, other than VRF multi-split | B | ≥70 kW and <223 kW | 11.7 | 10.9 | July 1, 2014 |
| 32. | Evaporation-cooled, other than VRF multi-split | B | ≥223 kW | 10.8 | 10.9 | January 1, 2013 |
| 33. | Water- or evaporation-cooled, VRF multi-split | A | ≥19 kW and <40 kW | 11.5 | 11.7 | January 1, 2013 |
| 34. | Water- or evaporation-cooled, VRF multi-split | A | ≥40 kW and <70 kW | 11.0 | 11.2 | January 1, 2013 |
| 35. | Water- or evaporation-cooled, VRF multi-split | A | ≥70 kW and <223 kW | 11.0 | 11.1 | January 1, 2013 |
| 36. | Water- or evaporation-cooled, VRF multi-split | A | ≥223 kW | 11.0 | 11.1 | January 1, 2013 |
| 37. | Water- or evaporation-cooled, VRF multi-split | B | ≥19 kW and <40 kW | 11.3 | 11.5 | January 1, 2013 |
| 38. | Water- or evaporation-cooled, VRF multi-split | B | ≥40 kW and <70 kW | 10.8 | 11.0 | January 1, 2013 |
| 39. | Water- or evaporation-cooled, VRF multi-split | B | ≥70 kW and <223 kW | 10.8 | 10.9 | January 1, 2013 |
| 40. | Water- or evaporation-cooled, VRF multi-split | B | ≥223 kW | 10.8 | 10.9 | January 1, 2013 |

* Note:  For the purposes of Column 3, “A” means either no heating section or an electric heating section and “B” means a heating section other than an electric heating section. Variable refrigerant flow multi-split air conditioners or heat pumps with heat recovery fall under the category of “B” unless they also have electric resistance heating, in which case they fall under the category of “A”.

table 2
Large unitary heat pumps

| Column 1 Item | Column 2 Sub-type | Column 3 Heating type | Column 4 Cooling capacity | Column 5 EER | Column 6 IEER | Column 7 COP at inlet air at 8.3C | Column 8 COP at inlet air at -8.3C | Column 9 Compliance date |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1. | Air-cooled | A | ≥19 kW and <40 kW | 11.0 | 11.2 | 3.30 | 2.25 | January 1, 2013 |
| 2. | Air-cooled | A | ≥40 kW and <70 kW | 10.6 | 10.7 | 3.20 | 2.05 | January 1, 2013 |
| 3. | Air-cooled | A | ≥70 kW and <223 kW | 9.5 | 9.6 | 3.20 | 2.05 | January 1, 2013 |
| 4. | Air-cooled | A | ≥223 kW | 9.5 | 9.6 | 3.20 | 2.05 | January 1, 2013 |
| 5. | Air-cooled | B | ≥19 kW and <40 kW | 10.8 | 11.0 | 3.30 | 2.25 | January 1, 2013 |
| 6. | Air-cooled | B | ≥40 kW and <70 kW | 10.4 | 10.5 | 3.20 | 2.05 | January 1, 2013 |
| 7. | Air-cooled | B | ≥70 kW and <223 kW | 9.3 | 9.4 | 3.20 | 2.05 | January 1, 2013 |
| 8. | Air-cooled | B | ≥223 kW | 9.3 | 9.4 | 3.20 | 2.05 | January 1, 2013 |
| 9. | Water-cooled, other than VRF multi-split | A | ≥19 kW and <40 kW | 12.1 | 11.2 | 3.30 | 2.25 | July 1, 2013 |
| 10. | Water-cooled, other than VRF multi-split | A | ≥40 kW and <70 kW | 11.0 | 10.7 | 3.20 | 2.05 | July 1, 2013 |
| 11. | Water-cooled, other than VRF multi-split | A | ≥40 kW and <70 kW | 12.5 | 10.7 | 3.20 | 2.05 | July 1, 2014 |
| 12. | Water-cooled, other than VRF multi-split | A | ≥70 kW and <223 kW | 11.0 | 9.6 | 3.20 | 2.05 | July 1, 2013 |
| 13. | Water-cooled, other than VRF multi-split | A | ≥70 kW and <223 kW | 12.4 | 9.6 | 3.20 | 2.05 | July 1, 2014 |
| 14. | Water-cooled, other than VRF multi-split | A | ≥223 kW | 9.5 | 9.6 | 3.20 | 2.05 | January 1, 2013 |
| 15. | Water-cooled, other than VRF multi-split | B | ≥19 kW and <40 kW | 11.9 | 11.0 | 3.30 | 2.25 | July 1, 2013 |
| 16. | Water-cooled, other than VRF multi-split | B | ≥40 kW and <70 kW | 11.0 | 10.5 | 3.20 | 2.05 | July 1, 2013 |
| 17. | Water-cooled, other than VRF multi-split | B | ≥40 kW and <70 kW | 12.3 | 10.5 | 3.20 | 2.05 | July 1, 2014 |
| 18. | Water-cooled, other than VRF multi-split | B | ≥70 kW and <223 kW | 10.8 | 9.4 | 3.20 | 2.05 | July 1, 2013 |
| 19. | Water-cooled, other than VRF multi-split | B | ≥70 kW and <223 kW | 12.2 | 9.4 | 3.20 | 2.05 | July 1, 2014 |
| 20. | Water-cooled, other than VRF multi-split | B | ≥223 kW | 9.3 | 9.4 | 3.20 | 2.05 | January 1, 2013 |
| 21. | Evaporation-cooled, other than VRF multi-split | A | ≥19 kW and <40 kW | 12.1 | 11.2 | 3.30 | 2.25 | July 1, 2013 |
| 22. | Evaporation-cooled, other than VRF multi-split | A | ≥40 kW and <70 kW | 11.0 | 10.7 | 3.20 | 2.05 | July 1, 2013 |
| 23. | Evaporation-cooled, other than VRF multi-split | A | ≥40 kW and <70 kW | 12.0 | 10.7 | 3.20 | 2.05 | July 1, 2014 |
| 24. | Evaporation-cooled, other than VRF multi-split | A | ≥70 kW and <223 kW | 11.0 | 9.6 | 3.20 | 2.05 | July 1, 2013 |
| 25. | Evaporation-cooled, other than VRF multi-split | A | ≥70 kW and <223 kW | 11.9 | 9.6 | 3.20 | 2.05 | July 1, 2014 |
| 26. | Evaporation-cooled, other than VRF multi-split | A | ≥223 kW | 9.5 | 9.6 | 3.20 | 2.05 | January 1, 2013 |
| 27. | Evaporation-cooled, other than VRF multi-split | B | ≥19 kW and <40 kW | 11.9 | 11.0 | 3.30 | 2.25 | July 1, 2013 |
| 28. | Evaporation-cooled, other than VRF multi-split | B | ≥40 kW and <70 kW | 11.0 | 10.5 | 3.20 | 2.05 | July 1, 2013 |
| 29. | Evaporation-cooled, other than VRF multi-split | B | ≥40 kW and <70 kW | 11.8 | 10.5 | 3.20 | 2.05 | July 1, 2014 |
| 30. | Evaporation-cooled, other than VRF multi-split | B | ≥70 kW and <223 kW | 10.8 | 9.4 | 3.20 | 2.05 | July 1, 2013 |
| 31. | Evaporation-cooled, other than VRF multi-split | B | ≥70 kW and <223 kW | 11.7 | 9.4 | 3.20 | 2.05 | July 1, 2014 |
| 32. | Evaporation-cooled, other than VRF multi-split | B | ≥223 kW | 9.3 | 9.4 | 3.20 | 2.05 | January 1, 2013 |
| 33. | Water- or evaporation-cooled, VRF multi-split | A | ≥19 kW and <40 kW | 12.0 | 11.2 | 3.30 | 2.25 | July 1, 2013 |
| 34. | Water- or evaporation-cooled, VRF multi-split | A | ≥40 kW and <70 kW | 10.6 | 10.7 | 3.20 | 2.05 | January 1, 2013 |
| 35. | Water- or evaporation-cooled, VRF multi-split | A | ≥70 kW and <223 kW | 9.5 | 9.6 | 3.20 | 2.05 | January 1, 2013 |
| 36. | Water- or evaporation-cooled, VRF multi-split | A | ≥70 kW and <223 kW | 10.0 | 9.6 | 3.20 | 2.05 | October 29, 2013 |
| 37. | Water- or evaporation-cooled, VRF multi-split | A | ≥223 kW | 9.5 | 9.6 | 3.20 | 2.05 | January 1, 2013 |
| 38. | Water- or evaporation-cooled, VRF multi-split | B | ≥19 kW and <40 kW | 12.0 | 11.0 | 3.30 | 2.25 | July 1, 2013 |
| 39. | Water- or evaporation-cooled, VRF multi-split | B | ≥40 kW and <70 kW | 10.4 | 10.5 | 3.20 | 2.05 | January 1, 2013 |
| 40. | Water- or evaporation-cooled, VRF multi-split | B | ≥70 kW and <223 kW | 9.3 | 9.4 | 3.20 | 2.05 | January 1, 2013 |
| 41. | Water- or evaporation-cooled, VRF multi-split | B | ≥70 kW and <223 kW | 9.8 | 9.4 | 3.20 | 2.05 | October 29, 2013 |
| 42. | Water- or evaporation-cooled, VRF multi-split | B | ≥223 kW | 9.3 | 9.4 | 3.20 | 2.05 | January 1, 2013 |
| 43. | Evaporation-cooled, VRF multi-split | A | ≥19 kW and <40 kW | 11.0 | 11.2 | 3.30 | 2.25 | January 1, 2013 |
| 44. | Evaporation-cooled, VRF multi-split | A | ≥40 kW and <70 kW | 10.6 | 10.7 | 3.20 | 2.05 | January 1, 2013 |
| 45. | Evaporation-cooled, VRF multi-split | A | ≥70 kW and <223 kW | 9.5 | 9.6 | 3.20 | 2.05 | January 1, 2013 |
| 46. | Evaporation-cooled, VRF multi-split | A | ≥223 kW | 9.5 | 9.6 | 3.20 | 2.05 | January 1, 2013 |
| 47. | Evaporation-cooled, VRF multi-split | B | ≥19 kW and <40 kW | 10.8 | 11.0 | 3.30 | 2.25 | January 1, 2013 |
| 48. | Evaporation-cooled, VRF multi-split | B | ≥40 kW and <70 kW | 10.4 | 10.5 | 3.20 | 2.05 | January 1, 2013 |
| 49. | Evaporation-cooled, VRF multi-split | B | ≥70 kW and <223 kW | 9.3 | 9.4 | 3.20 | 2.05 | January 1, 2013 |
| 50. | Evaporation-cooled, VRF multi-split | B | ≥223 kW | 9.3 | 9.4 | 3.20 | 2.05 | January 1, 2013 |

* Note:  For the purposes of Column 3, “A” means either no heating section or an electric heating section and “B” means a heating section other than an electric heating section. Variable refrigerant flow multi-split air conditioners or heat pumps with heat recovery fall under the category of “B” unless they also have electric resistance heating, in which case they fall under the category of “A”.

table 3
large condensing units

| Column 1 Item | Column 2 Sub-type | Column 3 Heating type | Column 4 Cooling capacity | Column 5 EER | Column 6 IEER | Column 7 COP at inlet air at 8.3C | Column 8 COP at inlet air at -8.3C | Column 9 Compliance date |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1. | Air-cooled | A or B | ≥19 kW and ≤70 kW | 10.1 | N/A | N/A | N/A | January 1, 2013 |
| 2. | Water- or evaporation-cooled | A or B | ≥19 kW and ≤70 kW | 13.1 | N/A | N/A | N/A | January 1, 2013 |

* Note:  For the purposes of Column 3, “A” means either no heating section or an electric heating section and “B” means a heating section other than an electric heating section. Variable refrigerant flow multi-split air conditioners or heat pumps with heat recovery fall under the category of “B” unless they also have electric resistance heating, in which case they fall under the category of “A”.

(5)  Sub-subparagraph 2.2 iv C of section 1 of Schedule 4 to the Regulation is amended by striking out “Table” and substituting “Tables”.

(6)  The Table to sub-subparagraph 2.2 iv C of section 1 of Schedule 4 to the Regulation is revoked and the following substituted:

table 1
Large unitary air conditioners

| Column 1 Item | Column 2 Sub-type | Column 3 Heating type | Column 4 Cooling capacity | Column 5 EER | Column 6 IEER |
| --- | --- | --- | --- | --- | --- |
| 1. | Air-cooled | A | ≥19 kW and <40 kW | 11.2 | 12.9 |
| 2. | Air-cooled | A | ≥40 kW and <70 kW | 11 | 12.4 |
| 3. | Air-cooled | A | ≥70 kW and <223 kW | 10.0 | 11.6 |
| 4. | Air-cooled | B | ≥19 kW and <40 kW | 11.0 | 12.7 |
| 5. | Air-cooled | B | ≥40 kW and <70 kW | 10.8 | 12.2 |
| 6. | Air-cooled | B | ≥70 kW and <223 kW | 9.8 | 11.4 |
| 7. | Water-cooled, other than VRF multi-split | A | ≥19 kW and <40 kW | 12.1 | 11.7 |
| 8. | Water-cooled, other than VRF multi-split | A | ≥40 kW and <70 kW | 12.5 | 11.2 |
| 9. | Water-cooled, other than VRF multi-split | A | ≥70 kW and <223 kW | 12.4 | 11.1 |
| 10. | Water-cooled, other than VRF multi-split | B | ≥19 kW and <40 kW | 11.9 | 11.5 |
| 11. | Water-cooled, other than VRF multi-split | B | ≥40 kW and <70 kW | 12.3 | 11.0 |
| 12. | Water-cooled, other than VRF multi-split | B | ≥70 kW and <223 kW | 12.2 | 10.9 |
| 13. | Evaporation-cooled, other than VRF multi-split | A | ≥19 kW and <40 kW | 12.1 | 11.7 |
| 14. | Evaporation-cooled, other than VRF multi-split | A | ≥40 kW and <70 kW | 12.0 | 11.2 |
| 15. | Evaporation-cooled, other than VRF multi-split | A | ≥70 kW and <223 kW | 11.9 | 11.1 |
| 16. | Evaporation-cooled, other than VRF multi-split | B | ≥19 kW and <40 kW | 11.9 | 11.5 |
| 17. | Evaporation-cooled, other than VRF multi-split | B | ≥40 kW and <70 kW | 11.8 | 11.0 |
| 18. | Evaporation-cooled, other than VRF multi-split | B | ≥70 kW and <223 kW | 11.7 | 10.9 |
| 19. | Water- or evaporation-cooled VRF multi-split | A | ≥19 kW and <40 kW | 11.5 | 11.7 |
| 20. | Water- or evaporation-cooled VRF multi-split | A | ≥40 kW and <70 kW | 11.0 | 11.2 |
| 21. | Water- or evaporation-cooled VRF multi-split | A | ≥70 kW and <223 kW | 11.0 | 11.1 |
| 22. | Water- or evaporation-cooled VRF multi-split | B | ≥19 kW and <40 kW | 11.3 | 11.5 |
| 23. | Water- or evaporation-cooled VRF multi-split | B | ≥40 kW and <70 kW | 10.8 | 11.0 |
| 24. | Water- or evaporation-cooled VRF multi-split | B | ≥70 kW and <223 kW | 10.8 | 10.9 |

* Note:  For the purposes of Column 3, “A” means either no heating section or an electric heating section and “B” means a heating section other than an electric heating section. Variable refrigerant flow multi-split air conditioners or heat pumps with heat recovery fall under the category of “B” unless they also have electric resistance heating, in which case they fall under the category of “A”.

table 2
Large unitary heat pumps

| Column 1 Item | Column 2 Sub-type | Column 3 Heating type | Column 4 Cooling capacity | Column 5 EER | Column 6 IEER | Column 7 COP at inlet air at 8.3C | Column 8 COP at inlet air at -8.3C |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 1. | Air-cooled | A | ≥19 kW and <40 kW | 11.0 | 12.2 | 3.3 | 2.25 |
| 2. | Air-cooled | A | ≥40 kW and <70 kW | 10.6 | 11.6 | 3.2 | 2.05 |
| 3. | Air-cooled | A | ≥70 kW and <223 kW | 9.5 | 10.6 | 3.2 | 2.05 |
| 4. | Air-cooled | B | ≥19 kW and <40 kW | 10.8 | 12.0 | 3.3 | 2.25 |
| 5. | Air-cooled | B | ≥40 kW and <70 kW | 10.4 | 11.4 | 3.2 | 2.05 |
| 6. | Air-cooled | B | ≥70 kW and <223 kW | 9.3 | 10.4 | 3.2 | 2.05 |
| 7. | Water-cooled, other than VRF multi-split | A | ≥19 kW and <40 kW | 12.1 | 11.2 | 3.30 | 2.25 |
| 8. | Water-cooled, other than VRF multi-split | A | ≥40 kW and <70 kW | 12.5 | 10.7 | 3.20 | 2.05 |
| 9. | Water-cooled, other than VRF multi-split | A | ≥70 kW and <223 kW | 12.4 | 9.6 | 3.20 | 2.05 |
| 10. | Water-cooled, other than VRF multi-split | B | ≥19 kW and <40 kW | 11.9 | 11.0 | 3.30 | 2.25 |
| 11. | Water-cooled, other than VRF multi-split | B | ≥40 kW and <70 kW | 12.3 | 10.5 | 3.20 | 2.05 |
| 12. | Water-cooled, other than VRF multi-split | B | ≥70 kW and <223 kW | 12.2 | 9.4 | 3.20 | 2.05 |
| 13. | Evaporation-cooled, other than VRF multi-split | A | ≥19 kW and <40 kW | 12.1 | 11.2 | 3.30 | 2.25 |
| 14. | Evaporation-cooled, other than VRF multi-split | A | ≥40 kW and <70 kW | 12.0 | 10.7 | 3.20 | 2.05 |
| 15. | Evaporation-cooled, other than VRF multi-split | A | ≥70 kW and <223 kW | 11.9 | 9.6 | 3.20 | 2.05 |
| 16. | Evaporation-cooled, other than VRF multi-split | B | ≥19 kW and <40 kW | 11.9 | 11.0 | 3.30 | 2.25 |
| 17. | Evaporation-cooled, other than VRF multi-split | B | ≥40 kW and <70 kW | 11.8 | 10.5 | 3.20 | 2.05 |
| 18. | Evaporation-cooled, other than VRF multi-split | B | ≥70 kW and <223 kW | 11.7 | 9.4 | 3.20 | 2.05 |
| 19. | Water- or evaporation-cooled VRF multi-split | A | ≥19 kW and <40 kW | 12.0 | 11.2 | 3.30 | 2.25 |
| 20. | Water- or evaporation-cooled VRF multi-split | A | ≥40 kW and <70 kW | 10.6 | 10.7 | 3.20 | 2.05 |
| 21. | Water- or evaporation-cooled VRF multi-split | A | ≥70 kW and <223 kW | 10.0 | 9.6 | 3.20 | 2.05 |
| 22. | Water- or evaporation-cooled VRF multi-split | B | ≥19 kW and <40 kW | 12.0 | 11.0 | 3.30 | 2.25 |
| 23. | Water- or evaporation-cooled VRF multi-split | B | ≥40 kW and <70 kW | 10.4 | 10.5 | 3.20 | 2.05 |
| 24. | Water- or evaporation-cooled VRF multi-split | B | ≥70 kW and <223 kW | 9.8 | 9.4 | 3.20 | 2.05 |

* Note:  For the purposes of Column 3, “A” means either no heating section or an electric heating section and “B” means a heating section other than an electric heating section. Variable refrigerant flow multi-split air conditioners or heat pumps with heat recovery fall under the category of “B” unless they also have electric resistance heating, in which case they fall under the category of “A”.

5.  Subparagraph 5 iv of section 1 of Schedule 6 to the Regulation is revoked and the following substituted:

iv.	Prescribed efficiency standard or requirement is that set out in the following Tables:

table 1
dry-type transformer – single phase, voltage class = 1.2 KV

| Column 1 Item | Column 2 kVA | Column 3 Efficiency at 0.35 of nameplate load (as percentage) |
| --- | --- | --- |
| 1. | 15 | 97.70 |
| 2. | 25 | 98.00 |
| 3. | 37.5 | 98.20 |
| 4. | 50 | 98.30 |
| 5. | 75 | 98.50 |
| 6. | 100 | 98.60 |
| 7. | 167 | 98.70 |
| 8. | 250 | 98.80 |
| 9. | 333 | 98.90 |

table 2
Dry-Type Transformer – Single Phase, Voltage Class > 1.2 kV

| Column 1 Item | Column 2 kVA | Column 3 BIL 20-45 kV, Efficiency at 0.5 of nameplate load (as percentage) | Column 4 BIL >45-95 kV, Efficiency at 0.5 of nameplate load (as percentage) | Column 5 BIL >95-199 kV, Efficiency at 0.5 of nameplate load (as percentage) |
| --- | --- | --- | --- | --- |
| 1. | 15 | 98.1 | 97.86 | 97.60 |
| 2. | 25 | 98.33 | 98.12 | 97.90 |
| 3. | 37.5 | 98.49 | 98.30 | 98.10 |
| 4. | 50 | 98.60 | 98.42 | 98.20 |
| 5. | 75 | 98.73 | 98.57 | 98.53 |
| 6. | 100 | 98.82 | 98.67 | 98.63 |
| 7. | 167 | 98.96 | 98.83 | 98.80 |
| 8. | 250 | 99.07 | 98.95 | 98.91 |
| 9. | 333 | 99.14 | 99.03 | 98.99 |
| 10. | 500 | 99.22 | 99.12 | 99.09 |
| 11. | 667 | 99.27 | 99.18 | 99.15 |
| 12. | 833 | 99.31 | 99.23 | 99.20 |

table 3
Dry-Type Transformer – Three Phase, Voltage Class = 1.2 kV

| Column 1 Item | Column 2 kVA | Column 3 Efficiency at 0.35 of nameplate load (as percentage) |
| --- | --- | --- |
| 1. | 15 | 97.89 |
| 2. | 30 | 98.23 |
| 3. | 45 | 98.40 |
| 4. | 75 | 98.60 |
| 5. | 112.5 | 98.74 |
| 6. | 150 | 98.83 |
| 7. | 225 | 98.94 |
| 8. | 300 | 99.02 |
| 9. | 500 | 99.14 |
| 10. | 750 | 99.23 |
| 11. | 1000 | 99.28 |

TABLE 4
Dry-Type Transformer – Three Phase, Voltage Class > 1.2 kV

| Column 1 Item | Column 2 kVA | Column 3 BIL 20-45 kV, Efficiency at 0.5 of nameplate load (as percentage) | Column 4 BIL >45-95 kV, Efficiency at 0.5 of nameplate load (as percentage) | Column 5 BIL >95-199 kV, Efficiency at 0.5 of nameplate load (as percentage) |
| --- | --- | --- | --- | --- |
| 1. | 15 | 97.50 | 97.18 | 96.80 |
| 2. | 30 | 97.90 | 97.63 | 97.30 |
| 3. | 45 | 98.10 | 97.86 | 97.60 |
| 4. | 75 | 98.33 | 98.13 | 97.90 |
| 5. | 112.5 | 98.52 | 98.36 | 98.10 |
| 6. | 150 | 98.65 | 98.51 | 98.20 |
| 7. | 225 | 98.82 | 98.69 | 98.57 |
| 8. | 300 | 98.93 | 98.81 | 98.69 |
| 9. | 500 | 99.09 | 98.99 | 98.89 |
| 10. | 750 | 99.21 | 99.12 | 99.02 |
| 11. | 1000 | 99.28 | 99.20 | 99.11 |
| 12. | 1500 | 99.37 | 99.30 | 99.21 |
| 13. | 2000 | 99.43 | 99.36 | 99.28 |
| 14. | 2500 | 99.47 | 99.41 | 99.33 |
| 15. | 3000 | 99.47 | 99.41 | 99.33 |
| 16. | 3750 | 99.47 | 99.41 | 99.33 |
| 17. | 5000 | 99.47 | 99.41 | 99.33 |
| 18. | 7500 | 99.48 | 99.41 | 99.39 |

6.  Subparagraph 7 i of section 1 of Schedule 7 to the Regulation is amended by striking out “June 13, 2018” and substituting “July 1, 2019”.

Commencement

7.  This Regulation comes into force on the later of July 1, 2017 and the day it is filed.

Back to top